OSM Data Model

Release 0

May 1, 2016

Table of Contents

NFV MANO Descriptors	3

ETSI MANO Common Object Models	4

Enhanced Platform Awareness Workload Placement	5

MANO Software Components	6

Network Service Descriptor	8

NS Connection Point	9

Virtual Link Descriptor	10

Constituent VNFD	11

NSD Placement Groups	11

Scaling Group	12

VNF Dependency	13

NSD Monitoring Parameter	13

Input Parameter xpath	16

Parameter Pool	16

Service Primitive	17

VNF Forwarding Graph Descriptor	19

Rendered Service Path	20

Classifier	20

Virtual Network Function Descriptor	22

VNFD Enhanced Platform Awareness Elements	23

Hugepages	24

CPU Pinning	24

Guest NUMA Awareness	24

PCI Pass-Through	25

Data Direct I/O	25

Cache Monitoring Technology	26

Cache Allocation Technology	26

VNFD Data Model	26

Management Interface	27

Internal VLD	32

VNFD Connection Point	32

VNFD Monitoring Parameter	32

VNFD Placement Groups	35

VDU Data Model	35

VM Flavor	37

vSwitch EPA	37

Hypervisor EPA	37

Host EPA	38

Guest EPA	40

VDU Internal Connection Point	43

VDU Internal Interface	43

VDU External Interface	44

VDU Dependency	44

MANO YANG Models	45

MANO Types	45

NSD YANG Model	72

VNFD YANG Model	85

# NFV MANO Descriptors

Today’s service providers have a growing interest in migrating custom, hardware-based network functions to the cloud. Cloud-based network functions—referred to as virtual network functions (VNFs)—are the software implementation of network functions that can be deployed on a network function virtualization infrastructure (NFVI). VNFs break the dependence on custom hardware appliances, allowing network functions, such as DNS, caching, and firewalls, to run in software.

This new cloud model paradigm is referred to as Network Function Virtualization (NFV).

NFV shows promise as a way to deliver VNFs on virtual machines on commodity off-the-shelf (COTS) infrastructure. NFV promises agile service delivery, faster development cycles, and optimal resource utilization. However, obstacles remain to successful NFV adoption, particularly for wireless and secure connectivity use cases at scale.

The promise of NFV can be realized only if the Virtual Network Function (VNF) applications behave in a way that can be easily deployed, scaled, and managed. This document describes various components of the ETSI MANO model. It also provides concrete data models for various descriptors, including VNF descriptor, Virtual Link Descriptor, VNF Forwarding Graph Descriptor, and Network Service descriptor.

# ETSI MANO Common Object Models

The ETSI MANO object models support simple onboarding, deployment, and management of virtual network functions. With extensive support for Enhanced Platform Awareness (EPA), the descriptors enable network function suppliers and network service providers to deploy virtual network functions quickly and easily, in the most cost-efficient manner.

VNF Descriptors (VNFDs) contain the attributes of a VNF necessary to define its platform resource requirements (CPU, memory, interfaces, network, and so on), plus special characteristics related to EPA attributes and performance capabilities.

Network Service Descriptors (NSDs) contain the attributes for a group of VNFs, which together constitute a service definition. These attributes contain the relationship requirements of the VNFs chained together as a service.

Virtual Link Descriptors (VLDs) define L2 or L3 links between VNFs in a chain and/or network interface boundaries (NIBs), which provide interconnectivity in and out of the platform.

Physical Network Function Descriptors (PNFDs) contain the attributes of a PNF necessary to integrate with legacy network hardware devices and to define its capabilities, networking requirements, and performance capabilities.

ETSI MANO objects are modeled as YANG objects, which the tool chain can automatically convert into NETCONF objects, XML objects, protocol buffers (protobufs), and GObject introspect-capable data objects by multiple languages (C, C++, Python, LUA).

The following advanced functions are supported:

- Maximize efficiency and performance by intelligently placing workloads on advanced NFV infrastructure capabilities, such as Enhanced Platform Awareness (EPA)

- Interface physical network functions (PNFs) and chain them together logically to create service chains made entirely of VNFs, PNFs, or combinations of both

See Also

Network Functions Virtualisation (NFV); Management and Orchestration; ETSI GS NFV-MAN 001 V1.1.1 (2014-12)

Network Functions Virtualisation (NFV); Architectural Framework; ETSI GS NFV 002 V1.2.1 (2014-12)

# Enhanced Platform Awareness Workload Placement

In a legacy, chassis-based architecture, network function suppliers have chosen a specific CPU for the network function. CPUs and the CPU cards are connected through a point-to-point, redundant fabric, such as a Dual Star backplane. The bandwidth and latency are guaranteed across the chassis fabric, and there is often a separate management fabric for separation of data and control. In such architecture, network functions do not have to deal with much variability.

By contrast, datacenter architectures are highly variable and nondeterministic. Virtual machines may be allocated from physical hosts anywhere within the same datacenter, and both the host and the physical links between these hosts can be oversubscribed. The CPU cores within a virtual machine might belong to different sockets on the physical host, leading to cache and memory access issues. This variability can lead to VNFs with completely different performance characteristics, even when they are placed in the same cloud infrastructure.

To ensure deterministic performance, OpenStack Enhanced Platform Awareness (EPA) attributes can increase the efficiency of the network function for high-touch tasks, such as packet forwarding and security. EPA attributes are discovered during the initial allocation of virtual machines from the Virtualized Infrastructure Manager (VIM).

During the VNF instantiation process, the VNF request characteristics are compared to the virtual machine capabilities in order to allocate workload placement across the corresponding VMs. This design supports advanced placement such as:

- Placing high data rate workloads, such as load balancing and bearer plane forwarding, on VMs that support NUMA affinity, hugepage setup, CPU pinning, and PCI pass through or single root I/O virtualization (SR-IOV)

- Placing best-effort workloads, such as statistics gathering or log output, on “vanilla” VMs

- Placing workloads that form part of the same network service (same service chain) in the same switching domain

- Distributing workloads, such as firewalling, DHCP, or other premise-related tasks, to a remote customer premise device

- Providing advanced security capabilities, such as Quick Assist Technology (QAT) crypto assist and Trusted Platform Module

# MANO Software Components

Virtualized Infrastructure Manager (VIM) is responsible for managing compute, network and storage resources. There can be many different implementations of VIM, including OpenStack, AWS and VMware. The VIM provides a northbound interface for the VNF Manager and NFV Orchestrator, and abstracts rest of the system from the details of underlying cloud management platform. The southbound interface should support Nf-Vi interface. The VNF Manager and NFV Orchestrator use the Vi-Vnfm and Or-Vi interfaces to interact with the VIM.

VNF Manager (VNFM) is the process of lifecycle management of the components and services. The VNFM oversees the lifecycle management of VNF instances, as well as:

- Starting the VNF from its descriptor and managing the VNF

- Scaling out/in and up/down of VNFs

- Monitoring and collecting parameters that determine the health of the VNF

NFV Orchestrator (NFV-O) is the process of creating virtual function instances to meet service requirements. The NFV-O manages network service lifecycle and resource orchestration across multiple VIMs. Other NFV-O functionality includes:

- Onboarding new network services and virtual network function packages

- Managing global resources (physical and logical network topology of how various VNFs and PNFs connect)

- Handling policy management related to scalability, reliability, and high availability for network service instances

- Authorizing network functions virtualization infrastructure resource requests

- Manages the NS service templates in the NS catalog

- Simplifies the job of launching new NSs

Reference: ETSI GS NFV 002 V1.2.1 (2014-12)

Designed with open, standards-based APIs, such as NETCONF and REST, and common information models, such as YANG, the Os-ma-nfvo interface is exposed through open, standards-based interfaces such as REST. This design enables upper-level orchestrators, such as Business Process Orchestrators or Service Orchestrators, to automate the entire service bring-up process.

# Network Service Descriptor

The Network Service Descriptor (NSD) is the top-level construct used for designing the service chains. The NSD is constructed by using other descriptors, including:

- VNF Descriptor (VNFD)

- PNF Descriptor (PNFD)

- Virtual Link Descriptor (VLD)

- VNF Forwarding Graph Descriptor (VNF-FGD)

The NSD references one or more VNFDs. These VNFs are connected VLDs, and the VNF-FGD determines the traffic flow in the service chain. In addition, the NSD exposes a set of connection points to enable connectivity to other Network Services or to the external world.

NSD Data Model

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| id | string | 1 | Unique identifier for the Network Service Descriptor (NSD). |
| name | string | 1 | NSD name. |
| short_name | string | 1 | NSD short name. |
| vendor | string | 1 | Vendor of the NSD. |
| logo | string | 1 | File path of the vendor-specific logo. For example, icons/mylogo.png The logo should be part of the network service package |
| description | string | 1 | Description of the NSD. |
| version | string | 1 | Version of the NSD. |
| connection-point | list | 0..n | List for network service (NS) connection points. Each NS has one or more external connection points used to link the NS to other NS or to external networks. Each NS exposes these connection points to the orchestrator. The orchestrator can construct network service chains by connecting the connection points between different NS. See "NS Connection Point " on page 9. |
| vld | list | 0..n | List of Virtual Link Descriptors (VLD). The VLD describes how VNFs in the NSD are connected. See "Virtual Link Descriptor" on page 10. |
| constituent-vnfd | list | 0..n | List of Virtual Network Function Descriptors (VNFDs) that are part of this network service. See "Constituent VNFD" on page 11 |
| scaling-group-descriptor | list | 0..n | Scaling group descriptor within this network service. Scaling group defines a group of VNFs, and the ratio of VNFs in the network service that is used as target for scaling action. See "Scaling Group" on page 12. |
| placement-groups | list | 0..n | List of placement groups at the NS level. See "NSD Placement Groups" on page 11. |
| vnf-dependency | list | 0..n | List of VNF dependencies. See "VNF Dependency " on page 13. |
| vnffgd | list | 0..n | List of VNF forwarding graph descriptor (VNFFD). See "VNF Forwarding Graph Descriptor" on page 19. |
| monitoring-param | grouping | 0..n | List of monitoring parameters at the NS level. See "NSD Monitoring Parameter " on page 13. |
| input-parameter-xpath | list | 0..n | List of xpath to parameters inside the NSD that can be customized during instantiation. See "Input Parameter xpath" on page 16. |
| parameter-pool | list | 0..n | Pool of parameter values from which configuration pulls. See "Parameter Pool" on page 16 |
| service-primitive | list | 0..n | Network service level configuration primitives. See "Service Primitive" on page 17. |

See Also

"MANO YANG Models" on page 45

"NSD YANG Model" on page 72

## NS Connection Point

A list for Network Service (NS) connection points. Each NS has one or more external connection points used to link the NS to other NS or to external networks. Each NS exposes these connection points to the orchestrator. The orchestrator can construct network service chains by connecting the connection points between different network services.

nsd:connection-point

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| name | string | 1 | Identifier for the external connection point. |
| type | enum | 1 | Type of connection point: VPORT: Virtual Port |

## Virtual Link Descriptor

A list of Virtual Link Descriptors (VLD). The VLD describes the basic topology of connectivity between one or more virtual network functions.

nsd:vld

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| id | string | 1 | Unique identifier for the VLD. |
| name | string | 1 | VLD name. |
| short_name | string | 1 | NSD short name |
| vendor | string | 1 | Vendor of the VLD. |
| description | string | 1 | Description of the VLD. |
| version | string | 1 | Version of the VLD. |
| type | enum | 1 | Type of the virtual link. ELAN: A multipoint service connecting a set of VNFs. |
| root-bandwidth | uint64 | 1 | For ELAN this is the aggregate bandwidth. |
| leaf-bandwidth | uint64 | 1 | For ELAN this is the bandwidth of branches. |
| vnfd-connection-point-ref | list | 0..n | Reference to VNFD connection points. See "nsd:vld:vnfd-connection-point-ref" below. |
| provider-network | container | 1 | Information about the provider network. See "nsd:vld:provider-network " on page 11. |

nsd:vld:vnfd-connection-point-ref

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| member-vnf-index-ref | reference | 1 | Reference to member-vnf within constituent units. path "../../../nsd:constituent-vndf/nsd:member-vnf-index" |
| vnf-id-ref | string | 1 | Reference to a VNFD. |
| vnfd-connection-point-ref | string | 1 | Reference to a connection point name in a VNFD. |

nsd:vld:provider-network

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| physical-network | string | 1 | Name of the physical network on which the provider network is built. |
| overlay-type | enum | 0..1 | Identifies the type of the overlay network. Value can be: LOCAL FLAT VLAN VXLAN GRE |
| segmentation-id | uint32 | 1 | Segmentation ID. |

## Constituent VNFD

A list of Virtual Network Function Descriptors (VNFDs) that are part of this network service.

nsd:constituent-vnfd

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| member-vnfd-index | uint64 | 1 | Identifier/index for the Virtual Network Function Descriptor (VNFD). This separate ID is required to ensure that multiple VNFs can be part of a single network service. |
| vnfd-id-ref | reference | 1 | Identifier for the VNFD. |
| start-by-default | boolean | 1 | VNFD is started as part of the NS instantiation. Default is true. |

## NSD Placement Groups

A list of placement groups at the network service level.

nsd:placement-groups

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| name | string | 1 | Place group construct to define the compute resource placement strategy in cloud environment. |
| requirement | string | 1 | This is free text space used to describe the intent/rationale behind this placement group. This is for human consumption only |
| strategy | enum | 1 | Strategy associated with this placement group. Following values are possible COLOCATION: [Default] Colocation strategy imply intent to share the physical infrastructure (hypervisor/network) among all members of this group. ISOLATION: Isolation strategy imply intent to not share the physical infrastructure (hypervisor/network) among the members of this group |
| constituent-vnfd | list | 0..n | List of VNFDs that are part of this placement group. See "nsd:placement-groups:constituent-vnfd" below. |

nsd:placement-groups:constituent-vnfd

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| member-vnf-index-ref | reference | 1 | Member VNF index of this member VNF. path "../../../constituent-vnfd/member-vnf-index" |
| vnfd-id-ref | reference | 1 | Identifier for the VNFD. path "/vnfd:vnfd-catalog/vnfd:vnfd/vnfd:id" |

## Scaling Group

The scaling group descriptor within this network service. A scaling group defines a group of VNFs and the ratio of VNFs in the network service that is used as target for scaling action.

nsd:scaling-group-descriptor

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| name | string | 1 | Name of the scaling group. |
| vnfd-member | list | 0..n | List of the VNFs in this scaling group. See "nsd:scaling-group-descriptor:vnfd-member" on page 13. |
| min-instance-count | uint32 | 1 | Minimum instances of the scaling group which are allowed. These instances are created by default when the network service is instantiated. Default is 0. |
| max-instance-count | uint32 | 1 | Maximum instance of this scaling group that are allowed in a single network service. The network service scaling will fail when the number of service group instances exceeds the max-instance-count specified. Default is 10. |
| scaling-config-action | list | 0..n | List of scaling config actions. See "nsd:scaling-group-descriptor:scaling-config-action" below. |

nsd:scaling-group-descriptor:vnfd-member

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| member-vnf-index-ref | reference | 1 | Member VNF index of this member VNF. path "../../../constituent-vnfd-member-vnfd-index" |
| count | uint32 | 1 | Count of this member VNF within this scaling group/ The count allows to define the number of instances when a scaling action targets this scaling group. Default is 1. |

nsd:scaling-group-descriptor:scaling-config-action

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| trigger | scaling-trigger | 1 | Scaling trigger. |
| ns-config-primitive-name-ref | reference | 1 | Reference to the NS config name primitive. path "../../../config-primitive/name |

## VNF Dependency

nsd:vnf-dependency

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| vnf-source-ref | reference | 1 | Reference to a VNFD. path "../../../vnfd:vnfd-catalog/vnfd:vnfd/vnfd:id" |
| vnf-depends-on-ref | reference | 1 | Reference to VNFD that on which the source VNF depends. path "../../../vnfd:vnfd-catalog/vnfd:vnfd/vnfd:id" |

## NSD Monitoring Parameter

nsd:monitoring-param

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| http-endpoint | list | 0..n | List of HTTP endpoints to be used by the monitoring parameters. See "nsd:monitoring-param:http-endpoint" on page 14 |
| monitoring-param | list | 0..n | List of monitoring params at the network service level. See "nsd:monitoring-param:monitoring-param" below |

nsd:monitoring-param:http-endpoint

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| path | string | 1 | The HTTP path on the management server. |
| https | boolean | 1 | Pick HTTPS instead of HTTP. Default is false. |
| port | inet:port-number | 1 | HTTP port to connect to. |
| username | string | 1 | HTTP basic auth user name. |
| password | string | 1 | HTTP basic auth password. |
| polling_interval_secs | uint8 | 1 | HTTP polling interval in seconds. Default is 2. |
| method | enum | 1 | Method to be performed at the URI. Values can be: GET (default) POST PUT GET DELETE PATCH OPTIONS |
| headers | list | 0..n | List of custom HTTP headers to put on the HTTP request. See "nsd:monitoring-param:http-endpoint:headers" below |

nsd:monitoring-param:http-endpoint:headers

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| key | string | 1 | HTTP header key. |
| value | string | 1 | HTTP header value. |

nsd:monitoring-param:monitoring-param

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| id | string | 1 | Unique identifier for the monitoring parameter. |
| name | string | 1 | Name of the monitoring parameter. |
| http-endpoint-ref | reference | 1 | path "../../../http-endpoint/path" |
| json-query-method | enum | 1 | The method to extract a value from a JSON response. NAMEKEY: [Default] Use the name as the key for a non-nested value. JSONPATH: Use jsonpath-rw implemenation to extract a value. OBJECTPATH: Use objectpath implemenation to extract a value. |
| json-query-params | container | 1 | Object for JSON query parameters. See "nsd:monitoring-param:monitoring-param:json-query-params" below |
| description | string | 1 | Description of the monitoring parameter. |
| group-tag | string | 1 | Tag to group monitoring parameters. |
| value-type | enum | 1 | The type of the parameter value. Value can be: INT (default) DECIMAL STRING |
| numeric-constraints | container | 1 | Constraints for the numbers. See "nsd:monitoring-param:monitoring-param:numeric-constraints" on page 16 |
| text-constraints | container | 1 | Constraints for the string. See "nsd:monitoring-param:monitoring-param:text-constraints" on page 16 |
| value-integer | int64 | 1 | Current value for integer parameter description. |
| value-decimal | decimal164 | 1 | Current value for decimal parameter. |
| value-string | string | 1 | Current value for the string parameter. |
| widget-type | enum | 1 | Type of the widget used by the RIFT.ware UI. Value can be: HISTOGRAM BAR GAUGE SLIDER COUNTER TEXTBOX |
| units | string | 1 | Units for the monitoring parameter, such as megabits per second. |

nsd:monitoring-param:monitoring-param:json-query-params

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| json-path | string | 1 | The JSON path used to extract value from the JSON structure. |
| object-path | string | 1 | The object path to use to extract value form the JSON structure. |

nsd:monitoring-param:monitoring-param:numeric-constraints

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| min-value | uint64 | 1 | Minimum value for the parameter. |
| max-value | uint64 | 1 | Maximum value for the parameter. |

nsd:monitoring-param:monitoring-param:text-constraints

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| min-length | uint8 | 1 | Minimum string length for the parameter. |
| max-length | uint8 | 1 | Maximum string length for the parameter. |

### Input Parameter xpath

nsd:input-parameter-xpath

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| xpath | string | 1 | An xpath that specifies the element in a descriptor. |
| label | string | 1 | A descriptive string. |
| default-value | string | 1 | A default value for this input parameter. |

## Parameter Pool

nsd:parameter-pool

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| name | string | 1 | Name of the configuration value pool. |
| range | container | 1 | Create a range of values from which to populate the pool. See "nsd:parameter-pool:range" below |

nsd:parameter-pool:range

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| start-value | uint32 | 1 | [Required] Generated pool values start at this value. |
| end-value | uint32 | 1 | [Required] Generated pool values end at this value. |

## Service Primitive

nsd:service-primitive

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| name | string | 1 | Name of the configuration primitive. |
| parameter | list | 0..n | List of parameters to the configuration primitive. See "nsd:service-primitive:parameter" below. |
| parameter-group | list | 0..n | Grouping of parameters that are logically grouped in UI. See "nsd:service-primitive:parameter-group" below. |
| vnf-primitive-group | list | 0..n | List of configuration primitives grouped by VNF. See "nsd:service-primitive:vnf-primitive-group" on page 18. |
| used-defined-script | string | 1 | A user defined script |

nsd:service-primitive:parameter

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| name | string | 1 | Name of parameter. |
| data-type | enum | 1 | Data type associated with the name. Value can be: STRING INTEGER BOOLEAN |
| mandatory | boolean | 1 | Specifies whether this field is mandatory. Default is false. |
| default-value | string | 1 | The default value for the field. |
| parameter-pool | string | 1 | NSD parameter pool name to use for this parameter. |
| read-only | boolean | 1 | The value should be dimmed by the UI. Applies only to parameters with default values. |
| hidden | boolean | 1 | The value should be hidden by the UI. Applies only to parameters with default values |

nsd:service-primitive:parameter-group

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| name | string | 1 | Name of parameter group. |
| parameter | list | 0..n | List of parameters to the configuration primitive. See "nsd:service-primitive:parameter-group:parameter" on page 18 |
| mandatory | boolean | 1 | Specifies whether this group mandatory. Default is true. |

nsd:service-primitive:parameter-group:parameter

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| name | string | 1 | Name of parameter. |
| data-type | enum | 1 | Data type associated with the name. Value can be: STRING INTEGER BOOLEAN |
| mandatory | boolean | 1 | Specifies whether this field is mandatory. Default is false. |
| default-value | string | 1 | The default value for the field. |
| parameter-pool | string | 1 | NSD parameter pool name to use for this parameter. |
| read-only | boolean | 1 | The value should be dimmed by the UI. Applies only to parameters with default values. |
| hidden | boolean | 1 | The value should be hidden by the UI. Applies only to parameters with default values |

nsd:service-primitive:vnf-primitive-group

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| member-vnf-index-ref | uint64 | 1 | Reference to member-vnf within constituent-vnfds. |
| vnfd-id-ref | string | 1 | A reference to a VNFD. |
| vnfd-name | string | 1 | Name of the VNFD. |
| primitive | list | 1 | A list of VNF primitives. See "nsd:service-primitive:vnf-primitive-group:primitive" below |

nsd:service-primitive:vnf-primitive-group:primitive

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| index | uint32 | 1 | Index of this primitive |
| name | string | 1 | Name of the primitive in the VNF primitive |

# VNF Forwarding Graph Descriptor

A Virtual Network Function Forwarding Graph (VNFFG) is a graph specified by a Network Service Provider of bi-directional logical links connecting NF nodes, where at least one node is a VNF through which network traffic is directed.

The VNFFG descriptor contains metadata about the VNF forwarding graph itself, as well as references to VLs, VNFs and PNFs, and network forwarding path elements. These elements include policies, such as MAC forwarding rules and routing entries, and references to connection points, such a virtual ports and virtual NIC addresses.

VNFFGD Data Model

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| id | string | 1 | Unique identifier for the VNFFGD. |
| name | string | 1 | VNFFGD name. |
| short_name | string | 1 | VNFFGD short name for the UI. |
| vendor | string | 1 | Provider of the VNFFGD. |
| description | string | 1 | Description of the VNFFGD. |
| version | string | 1 | Version of the VNFFGD. |
| rsp | list | 0..n | List of the Rendered Service Paths (RSP). See "Rendered Service Path" on page 20. |
| classifier | list | 0..n | List of classifier rules. See "Classifier" on page 20. |

See Also

"MANO YANG Models" on page 45

"NSD YANG Model" on page 72

## Rendered Service Path

vnffg:rsp

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| id | string | 1 | Unique identifier for the RSP. |
| name | string | 1 | RSP name. |
| vnfd-connection-point-ref | list | 0..n | See "vnffg:rsp:vnfd-connection-point-ref" below |

vnffg:rsp:vnfd-connection-point-ref

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| member-vnf-index-ref | reference | 1 | Reference to member VNF within constituent VNFDs path "../../../nsd:constituent-vnfd-nsd_member-vnf-index" |
| order | uint8 | 1 | A number that denotes the VNF in a chain. |
| vnfd-id-ref | string | 1 | A reference to a VNFD. |
| vnfd-connection-point-ref | string | 1 | A reference to a connection point name in a VNFD. |

## Classifier

vnffg:classifier

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| id | string | 1 | Unique identifier for the classifier rule. |
| name | string | 1 | Name of the classifier. |
| rsp-id-ref | reference | 1 | A reference to the RSP. path "../../nsd:rsp/nsd:id" |
| member-vnf-index-ref | reference | 1 | Reference to member-vnf within constituent-vndfs. path "../../../nsd:constituent-vnfd/nsd:member-vnf-index" |
| vnfd-id-ref | string | 1 | A reference to a VNFD. |
| vnfd-connection-point-ref | string | 1 | A reference to a connection point name in a VNFD. |
| match-atrributes | list | 0..n | List of match attributes. See "vnffg:classifier:match-attributes" on page 21. |

vnffg:classifier:match-attributes

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| id | string | 1 | Unique identifier for the classifier match-attribute rule. |
| ip-proto | uint8 | 1 | IP protocol |
| source-ip-address | inet:ip-address | 1 | Source IP address. |
| destination-ip-address | inet:ip-addres | 1 | Destination IP address. |
| source-port | inet:port-number | 1 | Source port. |
| destination-port | inet:port-number | 1 | Destination port. |

# Virtual Network Function Descriptor

The Virtual Network Function Descriptor (VNFD) describes the virtual network function and contains the following information:

- Individual VNF components that are part of the VNF

- Internal and external connectivity details

- KPI requirements and auto-scaling properties

The VNF Manager uses the VNFD to start a new instance of a VNF.

Each VNF is constructed from a set of discrete VNF Components (VNFCs). There can be one or more instance of each VNFC in the VNF. The VNFC is realized using a virtualized compute resource from the VIM. The virtualized compute resource can be either a Virtual Machine (VM) or a container. The VNFC includes a full description of software components that will run inside the virtualized compute resource.

The elements contained in the Virtual Deployment Unit (VDU) define the compute resource and software components. Specifically, VDU captures information about storage, memory, CPU, networking resources, and the software components inside the VM.

Each VNF has a set of internal and external connection points, which abstract the actual virtual interface used by the VM/container. The virtual interface in the VM is assigned a connection point. Internal connection points are used to connect the VNFC internals to the VNF. The connection points, whether internal or external, are connected using virtual links. Each virtual link has references to two or more connection points.

The following diagram illustrates how VNFs are connected using internal and external virtual links. VL1, VL2 and VL3 represent external virtual links. VL2 is used to connect the VNF1, VNF2 and VNF3. Virtual links VL1 and VL3 are used to connect the network services.

(Reference: ETSI GS NFV 001 V1.1.1 (2014-12))

The following diagram illustrates the high-level object model for the VNFD. The VNFD contains a list of VDUs, a list of internal connection points, a list of internal virtual links and a list of external connection points. The internal connection points and internal virtual links define how the VMs inside the VNF will be connected. The external connection points will be used by the NSD to chain VNFs. The VDUs define the individual VNF components. The VDU captures information about VM image, VM flavor, and EPA attributes.

(VNFD high-level object model)

## VNFD Enhanced Platform Awareness Elements

Enhanced Platform Awareness (EPA) is designed to improve the performance of guest virtual machines on the hypervisors by enabling fine-grained matching of workload requirements to platform capabilities, before the VM is launched. EPA includes the ability to:

- Launch cryptographic workload on a VM with cryptographic resources

- Launch high-bandwidth workload on a VM with DPDK capabilities

- Use vCPU to pCPU pinning and hugepages to improve NFV workload performance

- Configure PCI pass-through

EPA capabilities are captured in the VNFD Virtual Deployment Unit. The VNFD descriptor contains elements to capture these EPA attributes.

Note: On public clouds, such as AWS, many EPA features are not applicable.

### Hugepages

The use of hugepages can improve network performance. Because fewer pages are needed there are fewer Translation Look-aside Buffers (TLBs, high speed translation caches). Without standard 4k pages, high TLB miss rates could affect performance.

OpenStack hw:mem_page_size flavor filter supports the allocation of hugepages. The following page sizes are supported:

- Large (2MB or 1GB)

- Small (4K)

- Any

- 2MB

- 1GB

### CPU Pinning

Often in OpenStack deployments, hosts are configured to permit over-commit of CPUs. If conflict occurs between two guests VMs, there could be extended periods when the guest vCPU is not scheduled by the host. This scenario can result in unpredictable latency, which could affect certain types of workloads. To avoid a latency issue, the guest should be pinned to a dedicated physical CPU.

OpenStack hw:cpu_policy and hw:cpu_threads_policy filters control the CPU pinning behavior of the guest VMs. The hw:cpu_policy supports the shared and dedicated options. In the shared mode, the guest CPUs are not pinned to the physical CPUs. In the dedicated mode, the guest CPUs are pinned to the physical CPUs. For example, to launch a VM with vCPUs pinned to the physical CPUs, the following flavor key must be set:

hw:cpu_policy=dedicated

The hw:cpu_threads_policy supports avoid, separate, isolate, and prefer options. The avoid thread policy avoids placing the guest on a host with CPU threads. The separate thread policy places the vCPUs on different cores and avoids placing two vCPUs on two threads of the same core. The isolate policy places each vCPU on a different core, and places no vCPUs from a different guest on the same core. The prefer policy places the vCPUs on the same core.

### Guest NUMA Awareness

When running workloads on NUMA hosts, the CPUs executing the processes should be on the same node as the memory used. This configuration ensures that all memory accesses are local to the NUMA node and not consumed by the limited cross-node memory bandwidth, which adds latency to memory accesses. PCI devices are directly associated with specific NUMA nodes for the purposes of DMA. When you use PCI device assignment, place the guest VM on the same NUMA node as any device that is assigned to it. If the RAM/vCPUs associated with a flavor are larger than any single NUMA node, it is important to expose NUMA topology to the guest so that the guest operating system can schedule workloads it runs. For this setup to work, the guest NUMA nodes must be directly associated with host NUMA nodes.

OpenStack uses the following filters to configure the guest NUMA topology:

- hw:numa_nodes

- hw:numa_mempolicy

- hw:numa_cpus

- hw:numa_mem

Example

hw:numa_nodes=NN - numa of NUMA nodes to expose to the guest.
 hw:numa_mempolicy=preferred|strict - memory allocation policy
 hw:numa_cpus.0=<cpu-list> - mapping of vCPUS N-M to NUMA node
 hw:numa_cpus.1=<cpu-list> - mapping of vCPUS N-M to NUMA node 1
 hw:numa_mem.0=<ram-size> - mapping N GB of RAM to NUMA node 0 
 hw:numa_mem.1=<ram-size> - mapping N GB of RAM to NUMA node 1

The hw:numa_mempolicy is either preferred or strict. In the strict mode, the memory for the NUMA node in the guest must come from the corresponding NUMA node on the host.

### PCI Pass-Through

Guest virtual machines might need direct access to the PCI devices to avoid contention with other VMs. In addition, PCI pass-through significantly enhances performance since the hypervisor layer is bypassed. For example, PCI pass-through may be used to provide a guest exclusive and direct access to a NIC or Crypto resource.

OpenStack uses pci_pass-through:alias filter to assign a PCI device to the VM. This also requires configuration of PCI pass-through whitelist on each compute node and PCI pass-through alias on the controller node. The following examples show configuration of PCI pass-through whitelist and PCI alias.

pci_pass-through_whitelist=[{ "vendor_id":"8086","product_id":"1520"}] 
 pci_alias={"vendor_id":"8086", "product_id":"1520", "name":"a1"}

### Data Direct I/O

Intel Data Direct I/O (DDIO) enables Ethernet server NICs. Controllers talk directly to the processor cache without a detour through system memory. Intel DDIO makes the processor cache the primary destination and source of I/O data rather than main memory. By avoiding system memory, Intel DDIO reduces latency and increases system I/O. DDIO is enabled in the BIOS of the host.

### Cache Monitoring Technology

Cache Monitoring Technology (CMT) allows an operating system, hypervisor, or similar system management agent to determine the usage of cache based on applications running on the platform. The implementation is directed at L3 cache monitoring (currently the last-level cache in most server and client platforms).

### Cache Allocation Technology

Cache Allocation Technology (CAT) allows an operating system, hypervisor, or similar system management agent to specify the amount of L3 cache (currently the last-level cache in most server and client platforms) space an application can fill.

Note: As a hint to hardware functionality, certain features such as power management, may override CAT settings.

## VNFD Data Model

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| id | string | 1 | Identifier for the VNFD. |
| name | string | 1 | VNFD name. |
| short-name | string | 1 | VNFD short name. |
| vendor | string | 1 | Vendor of the VNFD. |
| logo | string | 1 | File path of the vendor-specific logo. For example, icons/mylogo.png The logo should be part of the VNF package. |
| description | string | 1 | Description of the VNFD. |
| version | string | 1 | Version of the VNFD. |
| mgmt-interface | container | 1 | Interface over which the VNF is managed. See "Management Interface" on page 27. |
| internal-vld | list | 0..n | A list of internal virtual links to connect various VNF components. The MANO document [1] refers this as “virtual-link”, however we are calling this field “internal-vlds” to explicitly indicate that these are internal virtual links. Also, we plan to use the same virtual link descriptor for both internal and external descriptors. If the VNF is composed of only one VNF component/VM, no internal VLD may be required. See "Internal VLD " on page 32. |
| connection-point | list | 0..n | The list for external connection points. Each VNF has one or more external connection points. As the name implies the external connection points are used for connecting the VNF to other VNFs or to external networks. Each VNF exposes these connection points to the orchestrator. The orchestrator can construct network services by connecting the connection points between different VNFs. The NFVO will use VLDs and VNFFGs at the network service level to construct network services. See "VNFD Connection Point " on page 32. |
| vdu | list | 0..n | List of virtual deployment units. See "VDU Data Model" on page 35. |
| vdu-dependency | list | 0..n | List of VDU dependencies. The orchestrator uses this list to determine the order of startup for VDUs. See "VDU Dependency " on page 44. |
| service-function-chain | enum | 1 | Type of node in Service Function Chaining Architecture. Type can be: UNAWARE (default) CLASSIFIER SF SFF |
| service-function-type | string | 1 | Type of service function. Note: This value needs to map with service function type in ODL to support VNFFG. Service Function Type is manadatory param in ODL SFC. This is temporarily set to string for ease of use. |
| monitoring-param | list | 0..n | List of monitoring parameters for the VNF. See "NSD Monitoring Parameter " on page 13. |
| placement-groups | list | 0..n | List of placement groups at the VNF level. See |

See Also

"MANO YANG Models" on page 45

"VNFD YANG Model" on page 85

### Management Interface

vnfd:mgmt-interface

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| vnf-configuration | container | 1 | Information regarding the VNF configuration is captured here. See "VNF Configuration" on page 29. |
| endpoint-type | choice | 1 | Indicates the type of management endpoint. Values can be: IP (see "vnfd:mgmt-interface:endpoint-type:ip" below) VDU-ID (see "vnfd:mgmt-interface:endpoint-type:vdu-id" below) CP (see "vnfd:mgmt-interface:endpoint-type:cp" below) |
| port | inet:port-number | 1 | Port number for the management interface. |
| dashboard-params | container | 1 | Parameters for the VNF dashboard. See "vnfd:mgmt-interface:dashboard-params" below. |

vnfd:mgmt-interface:endpoint-type:ip

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| ip | inet:ip-address | 1 | Specifies the static IP address for managing the VNF |

vnfd:mgmt-interface:endpoint-type:vdu-id

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| vdu-id | reference | 1 | Use the default management interface on this VDU. path "/vnfd:vnfd-catalog/vnfd:vnfd/vnfd:vdu/vnfd:id" |

vnfd:mgmt-interface:endpoint-type:cp

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| cp | reference | 1 | Use the ip address associated with this connection point. path "/vnfd:vnfd-catalog/vnfd:vnfd/vnfd:connection-point/vnfd:name" |

vnfd:mgmt-interface:dashboard-params

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| path | string | 1 | The HTTP path for the dashboard. |
| https | boolean | 1 | Pick HTTPS instead of HTTP. Default is false. |
| port | inet:port-number | 1 | The HTTP port for the dashboard |

#### VNF Configuration

vnfd:mgmt-interface:vnf-configuration

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| config-method | choice | 1 | Defines the configuration method for a VNF. Choices are: NETCONF (see "vnfd:mgmt-interface:config-method:netconf" below) REST (see "vnfd:mgmt-interface:config-method:rest" on page 30) SCRIPT (see "vnfd:mgmt-interface:config-method:script" on page 30) JUJU (see "vnfd:mgmt-interface:config-method:juju" on page 30) |
| config-access | container | 1 | IP address to be used to configure this VNF. Note: This parameter is optional if it is possible to dynamically resolve the IP. See "vnfd:mgmt-interface:vnf-configuration:config-access" on page 30 |
| input-params | container | 1 | Miscellaneous input parameters to be considered while processing the NSD to apply configuration. See "vnfd:mgmt-interface:vnf-configuration:input-params" on page 30. |
| config-attributes | container | 1 | Miscellaneous config attributes to be considered while processing the NSD to apply configuration. See "vnfd:mgmt-interface:vnf-configuration:config-atrributes" on page 30. |
| config-primitive | list | 0..n | List of configuration primitives supported by the configuration agent for this VNF. See "vnfd:mgmt-interface:vnf-configuration:config-primitive" on page 31 |
| initial-config-primitive | list | 0..n | Initial set of configuration primitives. See "vnfd:mgmt-interface:vnf-configuration:initial-config-primitive" on page 31. |
| config-template | string | 1 | Configuration template for each VNF. |

vnfd:mgmt-interface:config-method:netconf

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| target | enum | 1 | NETCONF configuration target. Values are: RUNNING CANDIDATE |
| protocol | enum | 1 | Protocol to use, such as for NETCONF. Values are: NONE SSH |
| port | inet:port-number | 1 | Port for the NETCONF server. |

vnfd:mgmt-interface:config-method:rest

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| port | inet_port-number | 1 | Port for the REST server |

vnfd:mgmt-interface:config-method:script

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| script-type | enum | 1 | Script type to use. Values are: BASH EXPECT |

vnfd:mgmt-interface:config-method:juju

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| charm | string | 1 | Juju charm to use to use with the VNF. |

vnfd:mgmt-interface:vnf-configuration:config-access

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| mgmt-ip-address | inet:ip-address | 1 | IP address to be used to configure this VNF. Optional if it is possible to resolve dynamically. |
| username | string | 1 | User name for configuration. |
| password | string | 1 | Password for configuration access authentication. |

vnfd:mgmt-interface:vnf-configuration:config-atrributes

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| config-priority | uint64 | 1 | Configuration priority, order of configuration to be applied to each VNF in this NS. A low number takes precedence over a high number. |
| config-delay | uint64 | 1 | Wait time (in seconds) before applying the configuration to this VNF. |

vnfd:mgmt-interface:vnf-configuration:input-params

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| config-priority | uint64 | 1 | Configuration priority , order of configuration to be applied to each VNF in this NS. A low number takes precedence over a high number. |
| config-delay | uint64 | 1 | Wait time (in seconds) before applying the configuration to this VNF. |

vnfd:mgmt-interface:vnf-configuration:config-primitive

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| name | string | 1 | Name of the configuration primitive. |
| parameter | list | 0..n | List of parameters to the configuration primitive. See "vnfd:mgmt-interface:vnf-configuration:config-primitive:parameter" below |

vnfd:mgmt-interface:vnf-configuration:config-primitive:parameter

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| name | string | 1 | Name of parameter |
| data-type | parameter-data-type | 1 | Data type associated with the name |
| mandatory | boolean | 1 | Defines whether this field is mandatory. Default is false. |
| default-value | string | 1 | The default value for the field. |
| parameter-pool | string | 1 | Parameter pool name to use for this parameter. |
| read-only | boolean | 1 | The value should be dimmed by the UI. Applies only to parameters with default values. |
| hidden | boolean | 1 | The value should be hidden by the UI. Applies only to parameters with default values. |

vnfd:mgmt-interface:vnf-configuration:initial-config-primitive

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| seq | uint64 | 1 | Sequence number for the configuration primitive. |
| name | string | 1 | Name of the configuration primitive. |
| parameter | list | 0..n | See "vnfd:mgmt-interface:vnf-configuration:config-primitive:parameter" above |

vnfd:mgmt-interface:vnf-configuration:initial-config-primitive:parameter

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| name | string | 1 | Name of the parameter. |
| value | string | 1 | Value of the parameter. |

### Internal VLD

vnfd:internal-vld

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| id | string | 1 | Unique identifier for the internal virtual link descriptor (VLD). |
| name | string | 1 | Name of the internal VLD. |
| short-name | string | 1 | Short name for the internal VLD. |
| description | string | 1 | Description of the internal VLD. |
| type | enum | 1 | Type of virtual link. Currently supports ELAN. ELAN is a multipoint service connecting a set of VDUs. |
| root-bandwidth | uint64 | 1 | For ELAN this is the aggregate bandwidth. |
| leaf-bandwidth | uint64 | 1 | For ELAN this is the bandwidth of branches. |
| internal-connection-point-ref | reference | 1 | Reference to one or more internal connection points. |

### VNFD Connection Point

vnfd:connection-point

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| name | string | 1 | Name of the connection point. |
| id | string | 1 | Unique identifier of the connection point |
| short-name | string | 1 | Short name of the connection point for display in the RIFT.ware UI. |
| type | enum | 1 | Type of connection point. ELAN: A multipoint service connecting a set of VNFs. |

### VNFD Monitoring Parameter

vnfd:monitoring-param

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| http-endpoint | list | 0..n | List of HTTP endpoints to be used by the monitoring parameters. See "vnfd:monitoring-param:http-endpoint" on page 33 |
| monitoring-param | list | 0..n | List of monitoring params at the network service level. See "vnfd:monitoring-param:monitoring-param" on page 33 |

vnfd:monitoring-param:http-endpoint

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| path | string | 1 | The HTTP path on the management server. |
| https | boolean | 1 | Pick HTTPS instead of HTTP. Default is false. |
| port | inet:port-number | 1 | HTTP port to connect to. |
| username | string | 1 | HTTP basic auth user name. |
| password | string | 1 | HTTP basic auth password. |
| polling_interval_secs | uint8 | 1 | HTTP polling interval in seconds. Default is 2. |
| method | enum | 1 | Method to be performed at the URI. Values can be: GET (default) POST PUT GET DELETE PATCH OPTIONS |
| headers | list | 0..n | List of custom HTTP headers to put on the HTTP request. See "vnfd:monitoring-param:http-endpoint:headers" below |

vnfd:monitoring-param:http-endpoint:headers

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| key | string | 1 | HTTP header key. |
| value | string | 1 | HTTP header value. |

vnfd:monitoring-param:monitoring-param

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| id | string | 1 | Unique identifier for the monitoring parameter. |
| name | string | 1 | Name of the monitoring parameter. |
| http-endpoint-ref | reference | 1 | path "../../../http-endpoint/path" |
| json-query-method | enum | 1 | The method to extract a value from a JSON response. NAMEKEY: [Default] Use the name as the key for a non-nested value. JSONPATH: Use jsonpath-rw implemenation to extract a value. OBJECTPATH: Use objectpath implemenation to extract a value. |
| json-query-params | container | 1 | Object for JSON query parameters. See "vnfd:monitoring-param:monitoring-param:json-query-params" below |
| description | string | 1 | Description of the monitoring parameter. |
| group-tag | string | 1 | Tag to group monitoring parameters. |
| value-type | enum | 1 | The type of the parameter value INT (default) DECIMAL STRING |
| numeric-constraints | container | 1 | Constraints for the numbers. See "vnfd:monitoring-param:monitoring-param:numeric-constraints" below |
| text-constraints | container | 1 | Constraints for the string. See "vnfd:monitoring-param:monitoring-param:text-constraints" on page 35 |
| value-integer | int64 | 1 | Current value for integer parameter description. |
| value-decimal | decimal164 | 1 | Current value for decimal parameter. |
| value-string | string | 1 | Current value for the string parameter. |
| widget-type | enum | 1 | Type of the widget used by the RIFT.ware UI. Value can be: HISTOGRAM BAR GAUGE SLIDER COUNTER TEXTBOX |
| units | string | 1 | Units for the monitoring parameter, such as megabits per second. |

vnfd:monitoring-param:monitoring-param:json-query-params

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| json-path | string | 1 | The JSON path used to extract value from the JSON structure. |
| object-path | string | 1 | The object path to use to extract value form the JSON structure. |

vnfd:monitoring-param:monitoring-param:numeric-constraints

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| min-value | uint64 | 1 | Minimum value for the parameter. |
| max-value | uint64 | 1 | Maximum value for the parameter. |

vnfd:monitoring-param:monitoring-param:text-constraints

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| min-length | uint8 | 1 | Minimum string length for the parameter. |
| max-length | uint8 | 1 | Maximum string length for the parameter. |

### VNFD Placement Groups

A list of placement groups at the VNF level.

vnfd:placement-groups

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| name | string | 1 | Place group construct to define the compute resource placement strategy in cloud environment. |
| requirement | string | 1 | This is free text space used to describe the intent/rationale behind this placement group. This is for human consumption only |
| strategy | enum | 1 | Strategy associated with this placement group. Following values are possible COLOCATION: [Default] Colocation strategy imply intent to share the physical infrastructure (hypervisor/network) among all members of this group. ISOLATION: Isolation strategy imply intent to not share the physical infrastructure (hypervisor/network) among the members of this group |
| constituent-vdus | list | 0..n | List of VDUs that are part of this placement group. See "vnfd:placement-groups:constituent-vdus" below. |

vnfd:placement-groups:constituent-vdus

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| member-vdu-ref | reference | 1 | Reference to the VDU in the VNF. path "../../../constituent-vnfd/member-vnf-index" |

## VDU Data Model

vnfd:vdu

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| id | string | 1 | Unique identifier for the Virtual Deployment Unit (VDU). |
| name | string | 1 | Unique name for the VDU. |
| description | string | 1 | Description of the VDU. |
| count | uint64 | 1 | Number of instances of the VDU. |
| mgmt-vpci | string | 1 | Specifies the virtual PCI address, expressed in the following format dddd:dd:dd.d. For example 0000:00:12.0. This information can be used to pass as metadata during the VM creation. |
| vm-flavor | container | 1 | Flavor of the VM, which captures information such as number of VCPUs, memory and disk space. See "VM Flavor " on page 37. |
| guest-epa | container | 1 | Captures guest EPA attributes. See "Guest EPA" on page 40. |
| vswitch-epa | container | 1 | Captures vSwitch EPA attributes. See "vSwitch EPA " on page 37. |
| hypervisor-epa | container | 1 | Captures hypervisor EPA attributes. See "Hypervisor EPA " on page 37. |
| host-epa | container | 1 | Captures host EPA attributes. See "Host EPA " on page 38. |
| image | string | 1 | [Required] File/URL path or name to the software image. If the image name is found within the VNF package, it will be uploaded to all cloud accounts during tje onboarding process. Otherwise, the image must be added to the cloud account with the same name as entered in this field. |
| image-checksum | string | 1 | Image md5sum for the software image. The md5sum, if provided, along with the image name uniquely identifies an image uploaded to the CAL. |
| cloud-init | string | 1 | Content of cloud-init script. |
| internal-connection-point | list | 0..n | List for internal connection points. Each VNFC has zero or more internal connection points. Internal connection points are used for connecting the VNF components internal to the VNF. If a VNF has only one VNFC, it may not have any internal connection points. See "VDU Internal Connection Point " on page 43. |
| internal-interface | list | 0..n | List of internal interfaces for the VNF. The external interfaces enable sending traffic to and from VNF. See "VDU Internal Interface " on page 43. |
| external-interface | list | 0..n | List of eternal interfaces for the VNF. See "VDU External Interface " on page 44. |

See Also

"MANO YANG Models" on page 45

"VNFD YANG Model" on page 85

### VM Flavor

vnfd:vdu:vm-flavor

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| vpcu-count | uint16 | 1 | Number of VCPUs for the VM. |
| memory-mb | uint16 | 1 | Amount of memory in MB. |
| storage-gb | uint16 | 1 | Amount of disk space in GB. |

### vSwitch EPA

vnfd:vdu:vswitch-epa

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| ovs-acceleration | enum | 0..1 | Specifies Open vSwitch acceleration mode. MANDATORY: OVS acceleration is required PREFERRED: OVS acceleration is preferred DISABLED: OVS acceleration is disabled. |
| ovs-offload | enum | 0..1 | Specifies Open vSwitch hardware offload mode. MANDATORY: OVS offload is required PREFERRED: OVS offload is preferred DISABLED: OVS offload is disabled |

### Hypervisor EPA

vnfd:vdu:hypervisor-epa

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| type | enum | 0..1 | Specifies the type of hypervisor. Value can be: KVM: KVM XEN: XEN |
| version | string | 1 | Version of the hypervisor. |

### Host EPA

Specifies the host level EPA attributes.

vnfd:vdu:host-epa

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| cpu-model | enum | 0..1 | Host CPU model. The following values are supported: PREFER_WESTMERE REQUIRE_WESTMERE PREFER_SANDYBRIDGE REQUIRE_SANDYBRIDGE PREFER_IVYBRIDGE REQUIRE_IVYBRIDGE PREFER_HASWELL REQUIRE_HASWELL PREFER_BROADWELL REQUIRE_BROADWELL PREFER_NEHALEM REQUIRE_NEHALEM PREFER_PENRYN REQUIRE_PENRYN PREFER_CONROE REQUIRE_CONROE PREFER_CORE2DUO REQUIRE_CORE2DUO |
| cpu-arch | enum | 0..1 | Host CPU architecture. The following values are supported: PREFER_X86 REQUIRE_X86 PREFER_X86_64 REQUIRE_X86_64 PREFER_I686 REQUIRE_I686 PREFER_IA64 REQUIRE_IA64 PREFER_ARMV7 REQUIRE_ARMV7 PREFER_ARMV8 REQUIRE_ARMV8 |
| cpu-vendor | enum | 0..1 | Host CPU vendor. The following values are supported: PREFER_INTEL REQUIRE_INTEL PREFER_AMD REQUIRE_AMD |
| cpu-socket-count | enum | 0..1 | Number of sockets on the host. The following values are supported: PREFER_ONE PREFER_TWO REQUIRE_ONE REQUIRE_TWO |
| cpu-core-count | uint64 | 1 | Number of cores on the host. |
| cpu-feature | enum | 0..1 | The following values are supported: PREFER_AES REQUIRE_AES PREFER_CAT REQUIRE_CAT PREFER_CMT REQUIRE_CMT PREFER_DDIO REQUIRE_DDIO NOTE: Provide both REQUIRE and PREFER options for these features. AES: CPU supports advanced instruction set for AES (Advanced Encryption Standard). CAT: Cache Allocation Technology (CAT) allows an operating system, hypervisor, or similar system management agent to specify the amount of L3 cache (currently the last-level cache in most server and client platforms) space an application can fill. As a hint to hardware functionality, certain features such as power management may override CAT settings). CMT: Cache Monitoring Technology (CMT) allows an Operating System, Hypervisor, or similar system management agent to determine the usage of cache based on applications running on the platform. The implementation is directed at L3 cache monitoring (currently the last-level cache in most server and client platforms). DDIO: Intel Data Direct I/O (DDIO) enables Ethernet server NICs and controllers talk directly to the processor cache without a detour via system memory. This enumeration specifies if the VM requires a DDIO capable host. |
| om-cpu-model-string | string | 1 | OpenMano CPU model string |
| om-cpu-feature | string | 1 | OpenMano CPU features |

### Guest EPA

EPA attributes for the guest.

vnfd:vdu:guest-epa

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| trusted-execution | boolean | 1 | This VM should be allocated from trusted pool. |
| mempage-size | enum | 0..1 | Memory page allocation size. If a VM requires hugepages, it should choose LARGE or SIZE_2MB or SIZE_1GB. If the VM prefers hugepages it should chose PREFER_LARGE. LARGE: Require hugepages (either 2MB or 1GB) SMALL: Doesn't require hugepages SIZE_2MB: Requires 2MB hugepages SIZE_1GB: Requires 1GB hugepages PREFER_LARGE: Application prefers hugepages |
| cpu-pinning-policy | enum | 0..1 | CPU pinning policy describes association between virtual CPUs in guest and the physical CPUs in the host. DEDICATED: Virtual CPUs are pinned to physical CPUs SHARED: Multiple VMs may share the same physical CPUs. ANY: (Default) Any policy is acceptable for the VM |
| cpu-thread-pinning-policy | enum | 0..1 | CPU thread pinning policy describes how to place the guest CPUs when the host supports hyper threads: AVOID: Avoids placing a guest on a host with threads. SEPARATE: Places vCPUs on separate cores, and avoids placing two vCPUs on two threads of same core. ISOLATE: Places each vCPU on a different core, and places no vCPUs from a different guest on the same core. PREFER: Attempts to place vCPUs on threads of the same core. |
| pcie-device | list | 0..1 | List of pcie passthrough devices. See "vnfd:vdu:guest-epa:pcie-device" below |
| numa-policy | choice | 1 | Specifies whether the VM is NUMA aware. When NUMA aware, the numa-node-policy container captures the details about the numa-node-policy. Choices are: NUMA-UNAWARE NUMA-AWARE |

vnfd:vdu:guest-epa:pcie-device

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| device-id | string | 1 | Device identifier |
| count | uint64 | 1 | Number of devices to attach to the VM. |

vnfd:vdu:guest-epa:numa-policy:numa-unaware

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| numa-unaware | empty | 1 | Specifies that no NUMA policy is requested. |

vnfd:vdu:guest-epa:numa-policy:numa-aware

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| numa-node-policy | container | 1 | This policy defines numa topology of the guest. Specifically identifies if the guest should be run on a host with one numa node or multiple numa nodes. As an example a guest may want 8 vcpus and 4 GB of memory. But may want the vcpus and memory distributed across multiple numa nodes. The NUMA node 1 may run with 6 vcpus and 3GB, and NUMA node 2 may run with 2 vcpus and 1GB. See "vnfd:vdu:guest-epa:numa-policy:numa-aware:numa-node-policy" below |

vnfd:vdu:guest-epa:numa-policy:numa-aware:numa-node-policy

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| node-cnt | uint16 | 1 | Number of NUMA nodes to expose to the VM. |
| mem-policy | enum | 1 | This policy specifies how the memory should be allocated in a multi-node scenario. STRICT: The memory must be allocated strictly from the memory attached to the NUMA node. PREFERRED: The memory should be allocated preferentially from the memory attached to the NUMA node |
| node | list | 0..n | List of NUMA nodes. See "vnfd:vdu:guest-epa:numa-policy:numa-aware:numa-node-policy:node" on page 42. |

vnfd:vdu:guest-epa:numa-policy:numa-aware:numa-node-policy:node

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| id | uint64 | 1 | NUMA node identification. Typically 0 or 1. |
| vpcu | list | 1 | List of VPCUs to allocate on this NUMA node. |
| memory-mb | uint64 | 1 | Memory size expressed in MB for this NUMA node. |
| om-numa-type | choice | 1 | Openmano NUMA type selection: CORES PAIRED-THREADS THREADS See "vnfd:vdu:guest-epa:numa-policy:numa-aware:numa-node-policy:node" above |

vnfd:vdu:guest-epa:numa-policy:numa-aware:numa-node-policy:node:om-numa-type:cores

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| num-cores | uint8 | 1 | Number of cores. |

vnfd:vdu:guest-epa:numa-policy:numa-aware:numa-node-policy:node:om-numa-type:paired-threads

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| num-paired-threads | uint8 | 1 | Number of paired-threads. |
| paired-thread-ids | list | 0..n | List of thread paired to use in case of paired thread NUMA. |

vnfd:vdu:guest-epa:numa-policy:numa-aware:numa-node-policy:node:om-numa-type:paired-threads:paired-thread-ids

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| thread-a | uint8 | 1 | Thread ID |
| thread-b | uint8 | 1 | Thread ID |

vnfd:vdu:guest-epa:numa-policy:numa-aware:numa-node-policy:node:om-numa-type:threads

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| nym-threads | uint8 | 1 | Number of threads. |

### VDU Internal Connection Point

vnfd:vdu:internal-connection-point

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| name | string | 1 | Name of the connection point. |
| id | string | 1 | Unique identifier for the connection point. |
| short-name | string | 1 | Short name of the connection point for display in the RIFT.wareUI. |
| type | enum | 1 | Type of connection point. ELAN: A multipoint service connecting a set of VNFs |
| internal-vld-ref | reference | 1 | path "../../../internal-vld/id" |

### VDU Internal Interface

vnfd:vdu:internal-interface

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| name | string | 1 | Name of the internal interface inside the VDU. Note: This name has only local significance to the VDU. |
| vdu-internal-connection-point-ref | reference | 1 | Reference to an internal connection point. path "../../internal-connection-point/id" |
| virtual-interface | container | 1 | Container for the virtual interface properties. See "vnfd:vdu:internal-interface:virtual-interface" below. |

vnfd:vdu:internal-interface:virtual-interface

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| type | enum | 1 | Specifies the type of virtual interface between VM and host. VIRTIO: Use the traditional VIRTIO interface PCI-PASSTHROUGH: Use PCI-PASSTHROUGH interface SR-IOV: Use SR-IOV interface OM-MGMT: Used to specify openmano mgmt internal-connection type |
| vpci | string | 1 | Specifies the virtual PCI address. Expressed in the following format dddd:dd:dd.d. For example 0000:00:12.0. This information can be used to pass as metadata during the VM creation |
| bandwidth | integer | 1 | Specifies the bandwidth requirement for the NIC. |

### VDU External Interface

vnfd:vdu:external-interface

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| name | string | 1 | Name of the external interface inside the VDU. Note: This name has only local significance. |
| vnfd-connection-point-ref | reference | 1 | Reference to a connection point. path "../../../connection-point/name" |
| virtual-interface | container | 1 | Container for the virtual interface properties. See "vnfd:vdu:external-interface:virtual-interface" below. |

vnfd:vdu:external-interface:virtual-interface

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| type | enum | 1 | Specifies the type of virtual interface between VM and host. VIRTIO: Use the traditional VIRTIO interface PCI-PASSTHROUGH: Use the PCI-PASSTHROUGH interface SR-IOV: Use the SR-IOV interface OM-MGMT: Used to specify openmano mgmt external-connection type |
| vpci | string | 1 | Specifies the virtual PCI address. Expressed in the following format dddd:dd:dd.d. For example 0000:00:12.0. This information can be used to pass as metadata during the VM creation |
| bandwidth | integer | 1 | Specifies the bandwidth requirement for the NIC. |

### VDU Dependency

vnfd:vdu-dependency

| ID | Type | Cardinality | Description |
| --- | --- | --- | --- |
| vdu-source-ref | reference | 1 | Identifier of the VDU. path "../../vdu/id" |
| vdu-depends-on-ref | reference | 1 | Reference to the VDU on which the source VDU depends. path "../../vdu/id" |

# MANO YANG Models

YANG is a data modeling language used to model configuration and state data manipulated by the Network Configuration (NETCONF) Protocol [RFC 6241], NETCONF remote procedure calls, and NETCONF notifications.

## MANO Types

module mano-types
 {
   namespace "urn:ietf:params:xml:ns:yang:nfvo:mano-types";
   prefix "manotypes";
 
   import ietf-inet-types {
     prefix "inet";
   }
 
   import rw-pb-ext {
     prefix "rwpb";
   }
 
   revision 2015-04-23 {
     description
       "Initial revision. This YANG file defines
        the reusable base types for VNF Management
        and Orchestration (MANO).";
     reference
       "Derived from earlier versions of base YANG files";
   }
 
   typedef parameter-data-type {
     type enumeration {
       enum string;
       enum integer;
       enum boolean;
     }
   }
 
   grouping primitive-parameter {
     leaf name {
       description
           "Name of the parameter.";
       type string;
     }
 
     leaf data-type {
       description
           "Data type associated with the name.";
       type manotypes:parameter-data-type;
     }
 
     leaf mandatory {
       description "Is this field mandatory";
       type boolean;
       default false;
     }
 
     leaf default-value {
       description "The default value for this field";
       type string;
     }
 
     leaf parameter-pool {
       description "NSD Parameter pool name to use for this paramter";
       type string;
     }
 
     leaf read-only {
       description
         "The value should be greyed out by the UI.
         Only applies to parameters with default values.";
       type boolean;
     }
 
     leaf hidden {
       description
         "The value should be hidden by the UI.
         Only applies to parameters with default values.";
       type boolean;
     }
   }
   
 
   grouping vnf-configuration {
     container vnf-configuration {
       rwpb:msg-new VnfConfiguration;
       description
           "Information regarding the VNF configuration 
            is captured here. Note that if the NS contains
            multiple instances of the same VNF, each instance
            of the VNF may have different configuration";
 
       choice config-method {
         description
             "Defines the configuration method for the VNF.";
         case netconf {
           description
               "Use NETCONF for configuring the VNF.";
           container netconf {
             leaf target {
               description
                   "Netconf configuration target";
               type enumeration {
                 enum running;
                 enum candidate;
               }
             }
 
             leaf protocol {
               description
                   "Protocol to use for netconf (e.g. ssh)";
               type enumeration {
                 enum None;
                 enum ssh;
               }
             }
 
             leaf port {
               description
                   "Port for the netconf server.";
               type inet:port-number;
             }
           }
         }
 
         case rest {
           description
               "Use REST for configuring the VNF.";
           container rest {
             leaf port {
               description
                   "Port for the REST server.";
               type inet:port-number;
             }
           }
         }
 
         case script {
           description
               "Use custom script for configuring the VNF.
                This script is executed in the context of 
                Orchestrator.";
           container script {
             leaf script-type {
               description
                   "Script type - currently supported : bash, expect";
               type enumeration {
                 enum bash;
                 enum expect;
               }
             }
           }
         }
 
         case juju {
           description
             "Configure the VNF through Juju.";
           container juju {
             leaf charm {
               description "Juju charm to use with the VNF.";
               type string;
             }
           }
         }
       }
 
       container config-access {
         leaf mgmt-ip-address {
           description
               "IP address to be used to configure this VNF,
                optional if it is possible to resolve dynamically.";
           type inet:ip-address;
         }
 
         leaf username {
           description 
               "username for configuration.";
           type string;
         }
 
         leaf password {
           description 
               "Password for configuration access authentication.";
           type string;
         }
       }
 
       container config-attributes {
         description
             "Miscelaneous input parameters to be considered
              while processing the NSD to apply configuration";
 
         leaf config-priority {
           description
               "Configuration priority - order of confgiration
                to be applied to each VNF in this NS,
                low number gets precedence over high number";
           type uint64;
         }
 
         leaf config-delay {
           description 
               "Wait (seconds) before applying the configuration to VNF";
           type uint64;
         }
       }
 
       list config-primitive {
         rwpb:msg-new ConfigPrimitive;
         description
             "List of configuration primitives supported by the
             configuration agent for this VNF.";
         key "name";
 
         leaf name {
           description
               "Name of the configuration primitive.";
           type string;
         }
 
         list parameter {
           description
               "List of parameters to the configuration primitive.";
           key "name";
           uses primitive-parameter;
         }
       }
 
       list initial-config-primitive {
         rwpb:msg-new InitialConfigPrimitive;
         description
             "Initial set of configuration primitives.";
         key "seq";
         leaf seq {
           description
               "Sequence number for the configuration primitive.";
           type uint64;
         }
 
         leaf name {
           description 
               "Name of the configuration primitive.";
           type string;
         }
 
         list parameter {
           key "name";
           leaf name {
             type string;
           }
 
           leaf value {
             type string;
           }
         }
       }
 
       leaf config-template {
         description
             "Configuration template for each VNF";
         type string;
       }
     }
   } // END - grouping vnf-configuration
 
   typedef virtual-link-type {
     description
         "Type of virtual link
          ELAN: A multipoint service connecting a set of VNFs
          // ELINE: For a simple point to point connection
          //        between a VNF and the existing network.
          // ETREE: A multipoint service connecting one or
          //        more roots and a set of leaves, but
          //        preventing inter-leaf communication.";
     type enumeration {
       enum ELAN;
       // enum ETREE;
       // enum ELINE;
     }
   }
 
   grouping named-value {
     leaf name {
       type string;
     }
 
     leaf value {
       type string;
     }
   }
 
   typedef http-method {
     description
       "Type of HTTP operation";
 
     type enumeration {
       enum POST;
       enum PUT;
       enum GET;
       enum DELETE;
       enum OPTIONS;
       enum PATCH;
     }
   }
 
   typedef api-type {
     description
       "Type of API to fetch monitoring params";
 
     type enumeration {
       enum HTTP;
       enum NETCONF;
       enum SOAP;
     }
   }
 
   typedef json-query-method {
     description
       "The method to extract a value from a JSON response
 
        NAMEKEY - Use the name as the key for a non-nested value.
        JSONPATH - Use jsonpath-rw implemenation to extract a value.
        OBJECTPATH - Use objectpath implemenation to extract a value.";
       type enumeration {
         enum NAMEKEY;
         enum JSONPATH;
         enum OBJECTPATH;
       }
   }
 
   typedef param-value-type {
     description
       "The type of the parameter value";
     type enumeration {
        enum INT;
        enum DECIMAL;
        enum STRING;
     }
   }
 
   typedef connection-point-type {
     description
         "Type of connection point
         VPORT: Virtual Port
         // VNIC_ADDR: Virtual NIC Address
         // PNIC_ADDR: Physical NIC Address
         // PPORT: Phsical Port.";
 
     type enumeration {
       enum VPORT;
     }
   }
 
   typedef widget-type {
     description
         "Type of the widget, typically used by the UI.";
     type enumeration {
       enum HISTOGRAM;
       enum BAR;
       enum GAUGE;
       enum SLIDER;
       enum COUNTER;
       enum TEXTBOX;
     }
   }
 
   typedef cpu-feature-type {
     description
         "Enumeration for CPU features.
 
          AES: CPU supports advanced instruction set for
          AES (Advanced Encryption Standard).
 
          CAT: Cache Allocation Technology (CAT) allows
          an Operating System, Hypervisor, or similar
          system management agent to specify the amount
          of L3 cache (currently the last-level cache
          in most server and client platforms) space an
          application can fill (as a hint to hardware
          functionality, certain features such as power
          management may override CAT settings).
 
          CMT: Cache Monitoring Technology (CMT) allows
          an Operating System, Hypervisor, or similar
          system management agent to determine the
          usage of cache based on applications running
          on the platform. The implementation is
          directed at L3 cache monitoring (currently
          the last-level cache in most server and
          client platforms).
 
          DDIO: Intel Data Direct I/O (DDIO) enables
          Ethernet server NICs and controllers talk
          directly to the processor cache without a
          detour via system memory. This enumeration
          specifies if the VM requires a DDIO
          capable host.";
 
     type enumeration {
       enum PREFER_AES;
       enum REQUIRE_AES;
       enum PREFER_CAT;
       enum REQUIRE_CAT;
       enum PREFER_CMT;
       enum REQUIRE_CMT;
       enum PREFER_DDIO;
       enum REQUIRE_DDIO;
     }
   }
 
   grouping vm-flavor {
     container vm-flavor {
       leaf vcpu-count {
         description
             "Number of vcpus for the VM.";
         type uint16;
       }
 
       leaf memory-mb {
         description
             "Amount of memory in MB.";
         type uint64;
       }
 
       leaf storage-gb {
         description
             "Amount of disk space in GB.";
         type uint64;
       }
     }
   } //grouping vm-flavor
 
   grouping vswitch-epa {
     container vswitch-epa {
       leaf ovs-acceleration {
         description
             "Specifies Open vSwitch acceleration mode.
              MANDATORY: OVS acceleration is required
              PREFERRED: OVS acceleration is preferred";
         type enumeration {
           enum MANDATORY;
           enum PREFERRED;
           enum DISABLED;
         }
       }
 
       leaf ovs-offload {
         description
             "Specifies Open vSwitch hardware offload mode.
              MANDATORY: OVS offload is required
              PREFERRED: OVS offload is preferred";
         type enumeration {
           enum MANDATORY;
           enum PREFERRED;
           enum DISABLED;
         }
       }
     }
   }
 
   grouping hypervisor-epa {
     container hypervisor-epa {
       leaf type {
         description
             "Specifies the type of hypervisor.
              KVM: KVM
              XEN: XEN";
         type enumeration {
           enum PREFER_KVM;
           enum REQUIRE_KVM;
         }
       }
       leaf version {
         type string;
       }
     }
   }
 
   grouping host-epa {
     container host-epa {
       description "Specifies the host level EPA attributes.";
       leaf cpu-model {
         description
             "Host CPU model. Examples include: SandyBridge,
              IvyBridge";
         type enumeration {
           enum PREFER_WESTMERE;
           enum REQUIRE_WESTMERE;
           enum PREFER_SANDYBRIDGE;
           enum REQUIRE_SANDYBRIDGE;
           enum PREFER_IVYBRIDGE;
           enum REQUIRE_IVYBRIDGE;
           enum PREFER_HASWELL;
           enum REQUIRE_HASWELL;
           enum PREFER_BROADWELL;
           enum REQUIRE_BROADWELL;
           enum PREFER_NEHALEM;
           enum REQUIRE_NEHALEM;
           enum PREFER_PENRYN;
           enum REQUIRE_PENRYN;
           enum PREFER_CONROE;
           enum REQUIRE_CONROE;
           enum PREFER_CORE2DUO;
           enum REQUIRE_CORE2DUO;
         }
       }
 
       leaf cpu-arch {
         description "Host CPU architecture.";
         type enumeration {
           enum PREFER_X86;
           enum REQUIRE_X86;
           enum PREFER_X86_64;
           enum REQUIRE_X86_64;
           enum PREFER_I686;
           enum REQUIRE_I686;
           enum PREFER_IA64;
           enum REQUIRE_IA64;
           enum PREFER_ARMV7;
           enum REQUIRE_ARMV7;
           enum PREFER_ARMV8;
           enum REQUIRE_ARMV8;
         }
       }
 
       leaf cpu-vendor {
         description "Host CPU Vendor.";
         type enumeration {
           enum PREFER_INTEL;
           enum REQUIRE_INTEL;
           enum PREFER_AMD;
           enum REQUIRE_AMD;
         }
       }
 
       leaf cpu-socket-count {
         description "Number of sockets on the host.";
         type enumeration {
           enum PREFER_ONE;
           enum PREFER_TWO;
           enum REQUIRE_ONE;
           enum REQUIRE_TWO;
         }
       }
 
       leaf cpu-core-count {
         description "Number of cores on the host.";
         type uint64;
       }
 
       leaf-list cpu-feature {
         description
             "List of CPU features.";
         type cpu-feature-type;
       }
 
       leaf om-cpu-model-string {
         description "Openmano CPU model string";
         type string;
       }
 
       leaf-list om-cpu-feature {
         description "Openmano CPU features";
         type string;
       }
     }
   }
 
   grouping guest-epa {
     description "EPA attributes for the guest";
     container guest-epa {
       leaf trusted-execution {
         description "This VM should be allocated from trusted pool";
         type boolean;
       }
 
       leaf mempage-size {
         description
             "Memory page allocation size. If a VM requires
              hugepages, it should choose LARGE or SIZE_2MB
              or SIZE_1GB. If the VM prefers hugepages it
              should chose PREFER_LARGE.
              LARGE        : Require hugepages (either 2MB or 1GB)
              SMALL        : Doesn't require hugepages
              SIZE_2MB     : Requires 2MB hugepages
              SIZE_1GB     : Requires 1GB hugepages
              PREFER_LARGE : Application perfers hugepages";
         type enumeration {
           enum LARGE;
           enum SMALL;
           enum SIZE_2MB;
           enum SIZE_1GB;
           enum PREFER_LARGE;
         }
       }
 
       leaf cpu-pinning-policy {
         description
             "CPU pinning policy describes association
              between virtual CPUs in guest and the
              physical CPUs in the host.
              DEDICATED : Virtual CPUs are pinned to
                          physical CPUs
              SHARED    : Multiple VMs may share the
                          same physical CPUs.
              ANY       : Any policy is acceptable for the VM";
         type enumeration {
           enum DEDICATED;
           enum SHARED;
           enum ANY;
         }
         default "ANY";
       }
 
       leaf cpu-thread-pinning-policy {
           description
             "CPU thread pinning policy describes how to
              place the guest CPUs when the host supports
              hyper threads:
              AVOID   : Avoids placing a guest on a host
                        with threads.
              SEPARATE: Places vCPUs on separate cores,
                        and avoids placing two vCPUs on
                        two threads of same core.
              ISOLATE : Places each vCPU on a different core,
                        and places no vCPUs from a different
                        guest on the same core.
              PREFER  : Attempts to place vCPUs on threads
                        of the same core.";
         type enumeration {
           enum AVOID;
           enum SEPARATE;
           enum ISOLATE;
           enum PREFER;
         }
       }
 
       list pcie-device {
         description
             "List of pcie passthrough devices.";
         key device-id;
         leaf device-id {
           description
               "Device identifier.";
           type string;
         }
         leaf count {
           description
               "Number of devices to attach to the VM.";
           type uint64;
         }
       }
 
       choice numa-policy {
         case numa-unware {
           leaf numa-unware {
             type empty;
           }
         }
 
         case numa-aware {
           container numa-node-policy {
             description
                 "This policy defines numa topology of the
                  guest. Specifically identifies if the guest
                  should be run on a host with one numa
                  node or multiple numa nodes. As an example
                  a guest may want 8 vcpus and 4 GB of
                  memory. But may want the vcpus and memory
                  distributed across multiple numa nodes.
                  The NUMA node 1 may run with 6 vcpus and
                  3GB, and NUMA node 2 may run with 2 vcpus
                  and 1GB.";
 
             leaf node-cnt {
               description
                   "The number of numa nodes to expose to the VM.";
               type uint16;
             }
 
             leaf mem-policy {
               description
                   "This policy specifies how the memory should
                    be allocated in a multi-node scenario.
                    STRICT    : The memory must be allocated
                                strictly from the memory attached
                                to the NUMA node.
                    PREFERRED : The memory should be allocated
                                perferentially from the memory
                                attached to the NUMA node";
               type enumeration {
                 enum STRICT;
                 enum PREFERRED;
               }
             }
 
            list node {
               key id;
               leaf id {
                 description
                     "NUMA node identification. Typically
                      it's 0 or 1";
                 type uint64;
               }
 
               leaf-list vcpu {
                 description
                     "List of vcpus to allocate on
                      this numa node.";
                 type uint64;
               }
 
               leaf memory-mb {
                 description
                     "Memory size expressed in MB
                      for this NUMA node.";
                 type uint64;
               }
 
               choice om-numa-type {
                 description
                     "Openmano Numa type selection";
 
                 case cores {
                   leaf num-cores {
                     type uint8;
                   }
                 }
 
                 case paired-threads {
                   container paired-threads {
                     leaf num-paired-threads {
                       type uint8;
                     }
 
                     list paired-thread-ids {
                       description
                           "List of thread pairs to use in case of paired-thread numa";
                       max-elements 16;
                       key thread-a;
 
                       leaf thread-a {
                           type uint8;
                       }
 
                       leaf thread-b {
                           type uint8;
                       }
                     }
                   }
                 }
                 case threads {
                   leaf num-threads {
                     type uint8;
                   }
                 }
               }
             }
 
           }
         }
       }
     }
   }
 
   grouping provider-network {
     container provider-network {
       description "Container for the provider network.";
       leaf physical-network {
         description
             "Name of the phsyical network on which the provider
              network is built.";
         type string;
       }
 
       leaf overlay-type {
         description
             "Type of the overlay network.";
         type enumeration {
           enum LOCAL;
           enum FLAT;
           enum VLAN;
           enum VXLAN;
           enum GRE;
         }
       }
       leaf segmentation_id {
         description
             "Segmentation ID";
             type uint32;
       }
     }
   }
 
   grouping monitoring-param {
     list http-endpoint {
       description
           "List of http endpoints to be used by monitoring params";
       key path;
 
       leaf path {
         description "The HTTP path on the management server";
         type string;
       }
 
       leaf https {
         description "Pick HTTPS instead of HTTP , Default is false";
         type boolean;
         default "false";
       }
 
       leaf port {
         description "The HTTP port to connect to";
         type inet:port-number;
       }
 
       leaf username {
         description "The HTTP basic auth username";
         type string;
       }
 
       leaf password {
         description "The HTTP basic auth password";
         type string;
       }
 
       leaf polling_interval_secs {
         description "The HTTP polling interval in seconds";
         type uint8;
         default 2;
       }
 
       leaf method {
         description
           "This is the method to be performed at the uri.
            GET by default for action";
 
         type manotypes:http-method;
         default "GET";
       }
 
       list headers {
         description "Custom HTTP headers to put on HTTP request";
         key key;
         leaf key{
           description "HTTP header key";
           type string;
         }
 
         leaf value{
           description "HTTP header value";
           type string;
         }
       }
     }
 
     list monitoring-param {
       description
           "List of monitoring parameters at the NS level";
       key id;
       leaf id {
         type string;
       }
 
       leaf name {
         type string;
       }
 
       leaf http-endpoint-ref {
         type leafref {
           path "../../http-endpoint/path";
         }
       }
 
       leaf json-query-method {
         type json-query-method;
         default "NAMEKEY";
       }
 
       container json-query-params {
         leaf json-path {
           description
             "The jsonpath to use to extract value from JSON structure";
           type string;
         }
         leaf object-path {
           description
             "The objectpath to use to extract value from JSON structure";
           type string;
         }
       }
 
       leaf description {
         type string;
       }
 
       leaf group-tag {
         description "A simple tag to group monitoring parameters";
         type string;
       }
 
       leaf value-type {
         type param-value-type;
         default "INT";
       }
 
       container numeric-constraints {
         leaf min-value {
           description
               "Minimum value for the parameter";
           type uint64;
         }
         leaf max-value {
           description
               "Maxium value for the parameter";
           type uint64;
         }
       }
 
       container text-constraints {
         leaf min-length {
           description
               "Minimum string length for the parameter";
           type uint8;
         }
         leaf max-length {
           description
               "Maximum string length for the parameter";
           type uint8;
         }
       }
 
       leaf value-integer {
         description
             "Current value for an integer parameter";
         type int64;
       }
 
       leaf value-decimal {
         description
             "Current value for a decimal parameter";
         type decimal64 {
           fraction-digits 4;
         }
       }
 
       leaf value-string {
         description
             "Current value for a string parameter";
         type string;
       }
 
       leaf widget-type {
         type manotypes:widget-type;
       }
 
       leaf units {
         type string;
       }
     }
   }
 
   grouping control-param {
     list control-param {
       description
           "List of control parameters to manage and
            update the running configuration of the VNF";
       key id;
 
       leaf id {
         type string;
       }
 
       leaf name {
         type string;
       }
 
       leaf description {
         type string;
       }
 
       leaf group-tag {
         description "A simple tag to group control parameters";
         type string;
       }
 
       leaf min-value {
         description
             "Minimum value for the parameter";
         type uint64;
       }
 
       leaf max-value {
         description
             "Maxium value for the parameter";
         type uint64;
       }
 
       leaf current-value {
         description
             "Current value for the parameter";
         type uint64;
       }
 
       leaf step-value {
         description
             "Step value for the parameter";
         type uint64;
       }
 
       leaf units {
         type string;
       }
 
       leaf widget-type {
         type manotypes:widget-type;
       }
 
       leaf url {
         description
           "This is the URL where to perform the operation";
 
         type inet:uri;
       }
 
       leaf method {
         description
           "This is the method to be performed at the uri.
            POST by default for action";
 
         type manotypes:http-method;
         default "POST";
       }
 
       leaf payload {
         description
           "This is the operation payload or payload template as stringified
            JSON. This field provides the data  to be sent for this operation
            call";
 
         type string;
       }
     }
   }
 
   grouping action-param {
     list action-param {
       description
           "List of action parameters to
            control VNF";
       key id;
       leaf id {
         type string;
       }
 
       leaf name {
         type string;
       }
 
       leaf description {
         type string;
       }
 
       leaf group-tag {
         description "A simple tag to group monitoring parameter";
         type string;
       }
 
       leaf url {
         description
           "This is the URL where to perform the operation";
         type inet:uri;
       }
 
       leaf method {
         description
           "This is the method to be performed at the uri.
            POST by default for action";
 
         type manotypes:http-method;
         default "POST";
       }
 
       leaf payload {
         description
           "This is the operation payload or payload template to be sent in
            the data for this operation call";
 
         type string;
       }
     }
   }
 
   grouping input-parameter {
     description "";
 
     list input-parameter {
       description
           "List of input parameters";
 
       key xpath;
 
 
       leaf xpath {
         description
           "A an xpath that specfies which element in a descriptor is to be
           modified.";
         type string;
       }
 
       leaf value {
         description
           "The value that the element specified by the xpath should take when a
           record is created.";
         type string;
       }
     }
   }
 
   grouping input-parameter-xpath {
     list input-parameter-xpath {
       description
           "List of xpaths to parameters inside the NSD
            the can be customized during the instantiation.";
 
       key "xpath";
       leaf xpath {
         description
             "An xpath that specifies the element in a descriptor.";
         type string;
       }
 
       leaf label {
         description "A descriptive string";
         type string;
       }
 
       leaf default-value {
         description " A default value for this input parameter";
         type string;
       }
     }
   }
 
   grouping nfvi-metrics {
     container vcpu {
       leaf label {
         description
           "Label to show in UI";
         type string;
         default "VCPU";
       }
 
       leaf total {
         description
           "The total number of VCPUs available.";
         type uint64;
       }
 
       leaf utilization {
         description
           "The VCPU utilization (percentage).";
         type decimal64 {
           fraction-digits 2;
           range "0 .. 100";
         }
       }
     }
 
     container memory {
       leaf label {
         description
           "Label to show in UI";
         type string;
         default "MEMORY";
       }
 
       leaf used {
         description
           "The amount of memory (bytes) currently in use.";
         type uint64;
       }
 
       leaf total {
         description
           "The amount of memory (bytes) available.";
         type uint64;
       }
 
       leaf utilization {
         description
           "The memory utilization (percentage).";
         type decimal64 {
           fraction-digits 2;
           range "0 .. 100";
         }
       }
     }
 
     container storage {
       leaf label {
         description
           "Label to show in UI";
         type string;
         default "STORAGE";
       }
 
       leaf used {
         description
           "The amount of storage (bytes) currently in use.";
         type uint64;
       }
 
       leaf total {
         description
           "The amount of storage (bytes) available.";
         type uint64;
       }
 
       leaf utilization {
         description
           "The storage utilization (percentage).";
         type decimal64 {
           fraction-digits 2;
           range "0 .. 100";
         }
       }
     }
 
     container external-ports {
       leaf label {
         description
           "Label to show in UI";
         type string;
         default "EXTERNAL PORTS";
       }
 
       leaf total {
         description
           "The total number of external ports.";
         type uint64;
       }
     }
 
     container internal-ports {
       leaf label {
         description
           "Label to show in UI";
         type string;
         default "INTERNAL PORTS";
       }
 
       leaf total {
         description
           "The total number of internal ports.";
         type uint64;
       }
     }
 
     container network {
       leaf label {
         description
           "Label to show in UI";
         type string;
         default "NETWORK TRAFFIC";
       }
 
       container incoming {
         leaf label {
           description
             "Label to show in UI";
           type string;
           default "INCOMING NETWORK TRAFFIC";
         }
 
         leaf bytes {
           description
             "The cumulative number of incoming bytes.";
           type uint64;
         }
 
         leaf packets {
           description
             "The cumulative number of incoming packets.";
           type uint64;
         }
 
         leaf byte-rate {
           description
             "The current incoming byte-rate (bytes per second).";
           type decimal64 {
             fraction-digits 2;
           }
         }
 
         leaf packet-rate {
           description
             "The current incoming packet (packets per second).";
           type decimal64 {
             fraction-digits 2;
           }
         }
       }
 
       container outgoing {
         leaf label {
           description
             "Label to show in UI";
           type string;
           default "OUTGOING NETWORK TRAFFIC";
         }
 
         leaf bytes {
           description
             "The cumulative number of outgoing bytes.";
           type uint64;
         }
 
         leaf packets {
           description
             "The cumulative number of outgoing packets.";
           type uint64;
         }
 
         leaf byte-rate {
           description
             "The current outgoing byte-rate (bytes per second).";
           type decimal64 {
             fraction-digits 2;
           }
         }
 
         leaf packet-rate {
           description
             "The current outgoing packet (packets per second).";
           type decimal64 {
             fraction-digits 2;
           }
         }
       }
     }
   }
 
   typedef alarm-severity-type {
     description "An indication of the importance or ugency of the alarm";
     type enumeration {
       enum LOW;
       enum MODERATE;
       enum CRITICAL;
     }
   }
 
   typedef alarm-metric-type {
     description "The type of metrics to register the alarm for";
     type enumeration {
       enum CPU_UTILIZATION;
       enum MEMORY_UTILIZATION;
       enum STORAGE_UTILIZATION;
     }
   }
 
   typedef alarm-statistic-type {
     description
         "The type of statistic to used to measure a metric to determine
         threshold crossing for an alarm.";
     type enumeration {
       enum AVERAGE;
       enum MINIMUM;
       enum MAXIMUM;
       enum COUNT;
       enum SUM;
     }
   }
 
   typedef alarm-operation-type {
     description
         "The relational operator used to define whether an alarm should be
         triggered when, say, the metric statistic goes above or below a
         specified value.";
     type enumeration {
       enum GE; // greater than or equal
       enum LE; // less than or equal
       enum GT; // greater than
       enum LT; // less than
       enum EQ; // equal
     }
   }
 
   grouping alarm {
     leaf alarm-id {
       description
           "This field is reserved for the identifier assigned by the cloud
           provider";
 
       type string;
     }
 
     leaf name {
       description "A human readable string to identify the alarm";
       type string;
     }
 
     leaf description {
       description "A string containing a description of this alarm";
       type string;
     }
 
     container actions {
       list ok {
         key "url";
         leaf url {
           type string;
         }
       }
 
       list insufficient-data {
         key "url";
         leaf url {
           type string;
         }
       }
 
       list alarm {
         key "url";
         leaf url {
           type string;
         }
       }
     }
 
     leaf repeat {
       description
           "This flag indicates whether the alarm should be repeatedly emitted
           while the associated threshold has been crossed.";
 
       type boolean;
       default true;
     }
 
     leaf enabled {
       description
           "This flag indicates whether the alarm has been enabled or
           disabled.";
 
       type boolean;
       default true;
     }
 
     leaf severity {
       description "A measure of the important or urgency of the alarm";
       type alarm-severity-type;
     }
 
     leaf metric {
       description "The metric to be tracked by this alarm.";
       type alarm-metric-type;
     }
 
     leaf statistic {
       description "The type of metric statistic that is tracked by this alarm";
       type alarm-statistic-type;
     }
 
     leaf operation {
       description
           "The relational operator that defines whether the alarm should be
           triggered when the metric statistic is, say, above or below the
           specified threshold value.";
       type alarm-operation-type;
     }
 
     leaf value {
       description
           "This value defines the threshold that, if crossed, will trigger
           the alarm.";
       type decimal64 {
         fraction-digits 4;
       }
     }
 
     leaf period {
       description
           "The period defines the length of time (seconds) that the metric
           data are collected over in oreder to evaluate the chosen
           statistic.";
       type uint32;
     }
 
     leaf evaluations {
       description
           "This is the number of samples of the metric statistic used to
           evaluate threshold crossing. Each sample or evaluation is equal to
           the metric statistic obtained for a given period. This can be used
           to mitigate spikes in the metric that may skew the statistic of
           interest.";
       type uint32;
     }
   }
 
   grouping placement-group-info {
     description "";
 
     leaf name {
       description
           "Place group construct to define the compute resource placement strategy
            in cloud environment";
       type string;
     }
 
     leaf requirement {
       description "This is free text space used to describe the intent/rationale
                    behind this placement group. This is for human consumption only";
       type string;
     }
     
     leaf strategy {
       description
           "Strategy associated with this placement group
              Following values are possible
                - COLOCATION: Colocation strategy imply intent to share the physical
                              infrastructure (hypervisor/network) among all members
                              of this group.
                - ISOLATION: Isolation strategy imply intent to not share the physical
                             infrastructure (hypervisor/network) among the members
                             of this group.
              ";
       type enumeration {
         enum COLOCATION;
         enum ISOLATION;
       }
       default "COLOCATION";
     }
   }
 }

## NSD YANG Model

module nsd
 {
   namespace "urn:ietf:params:xml:ns:yang:nfvo:nsd";
   prefix "nsd";
 
   import rw-pb-ext {
     prefix "rwpb";
   }
 
   import vld {
     prefix "vld";
   }
 
   import vnfd {
     prefix "vnfd";
   }
 
   import ietf-inet-types {
     prefix "inet";
   }
 
   import ietf-yang-types {
     prefix "yang";
   }
 
   import mano-types {
     prefix "manotypes";
   }
 
   revision 2014-10-27 {
     description
       "Initial revision. This YANG file defines
        the Network Service Descriptor (NSD)";
     reference
       "Derived from earlier versions of base YANG files";
   }
 
   typedef scaling-trigger {
     type enumeration {
       enum pre-scale-in {
         value 1;
       }
       enum post-scale-in {
         value 2;
       }
       enum pre-scale-out {
         value 3;
       }
       enum post-scale-out {
         value 4;
       }
     }
   }
 
   container nsd-catalog {
 
     list nsd {
       key "id";
 
       leaf id {
         description "Identifier for the NSD.";
         type yang:uuid;
       }
 
       leaf name {
         description "NSD name.";
         mandatory true;
         type string;
       }
 
       leaf short-name {
         description "NSD short name.";
         type string;
       }
 
 
       leaf vendor {
         description "Vendor of the NSD.";
         type string;
       }
       
       leaf logo {
         description
           "Vendor logo for the Network Service";
         type string;
       }
       
       leaf description {
         description "Description of the NSD.";
         type string;
       }
 
       leaf version {
         description "Version of the NSD";
         type string;
       }
 
       list connection-point {
         description
             "List for external connection points.
             Each NS has one or more external connection
             points. As the name implies that external
             connection points are used for connecting
             the NS to other NS or to external networks.
             Each NS exposes these connection points to
             the orchestrator. The orchestrator can
             construct network service chains by
             connecting the connection points between
             different NS.";
 
         key "name";
         leaf name {
           description
               "Name of the NS connection point.";
           type string;
         }
 
         leaf type {
           description
               "Type of the connection point.";
           type manotypes:connection-point-type;
         }
       }
 
       leaf-list vld-ref {
         type leafref {
           path "/vld:vld-catalog/vld:vld/vld:id";
         }
       }
 
       /* Still having issues modelling this,
          see the comments under vnfd-connection-point-ref
        */
       list vld {
         description
             "List of Virtual Link Descriptors.";
 
         key "id";
 
         leaf id {
           description 
               "Identifier for the VLD.";
           type string;
         }
 
         leaf name {
           description 
               "Virtual Link Descriptor (VLD) name.";
           type string;
         }
 
         leaf short-name {
           description 
               "Short name for VLD for UI";
           type string;
         }
 
         leaf vendor {
           description "Provider of the VLD.";
           type string;
         }
 
         leaf description {
           description "Description of the VLD.";
           type string;
         }
 
         leaf version {
           description "Version of the VLD";
           type string;
         }
 
         leaf type {
           type manotypes:virtual-link-type;
         }
 
         leaf root-bandwidth {
           description
               "For ELAN this is the aggregate bandwidth.";
           type uint64;
         }
 
         leaf leaf-bandwidth {
           description
               "For ELAN this is the bandwidth of branches.";
           type uint64;
         }
 
         list vnfd-connection-point-ref {
           description
               "A list of references to connection points.";
           key "member-vnf-index-ref";
 
           leaf member-vnf-index-ref {
             description "Reference to member-vnf within constituent-vnfds";
             type leafref {
               path "../../../nsd:constituent-vnfd/nsd:member-vnf-index";
             }
           }
 
            leaf vnfd-id-ref {
              description 
                  "A reference to a vnfd. This is a 
                   leafref to path:
                       ../../../nsd:constituent-vnfd
                       + [nsd:id = current()/../nsd:id-ref]
                       + /nsd:vnfd-id-ref
                   NOTE: An issue with confd is preventing the
                   use of xpath. Seems to be an issue with leafref
                   to leafref, whose target is in a different module.
                   Once that is resovled this will switched to use
                   leafref";
              type yang:uuid;
            }
 
            leaf vnfd-connection-point-ref {
              description 
                  "A reference to a connection point name 
                   in a vnfd. This is a leafref to path:
                       /vnfd:vnfd-catalog/vnfd:vnfd
                       + [vnfd:id = current()/../nsd:vnfd-id-ref]
                       + /vnfd:connection-point/vnfd:name
                   NOTE: An issue with confd is preventing the
                   use of xpath. Seems to be an issue with leafref
                   to leafref, whose target is in a different module.
                   Once that is resovled this will switched to use
                   leafref";
               type string;
           }
         }
 
         // replicate for pnfd container here
         uses manotypes:provider-network;
       }
 
       list constituent-vnfd {
         description
             "List of VNFDs that are part of this
             network service.";
 
         key "member-vnf-index";
 
         leaf member-vnf-index {
           description
             "Identifier/index for the VNFD. This separate id
              is required to ensure that multiple VNFs can be
              part of single NS";
           type uint64;
         }
 
         leaf vnfd-id-ref {
           description
             "Identifier for the VNFD.";
           type leafref {
             path "/vnfd:vnfd-catalog/vnfd:vnfd/vnfd:id";
           }
         }
 
         leaf start-by-default {
           description
             "VNFD is started as part of the NS instantiation";
           type boolean;
           default true;
         }
 
         // Provide this VNF configuration parameters
         uses manotypes:vnf-configuration;
       }
 
       list scaling-group-descriptor {
         description
             "scaling group descriptor within this network service.
              The scaling group defines a group of VNFs,
              and the ratio of VNFs in the network service
              that is used as target for scaling action";
 
         key "name";
 
         leaf name {
           description "Name of this scaling group.";
           type string;
         }
 
         list vnfd-member {
           description "List of VNFs in this scaling group";
           key "member-vnf-index-ref";
 
           leaf member-vnf-index-ref {
             description "member VNF index of this member VNF";
             type leafref {
               path "../../../constituent-vnfd/member-vnf-index";
             }
           }
 
           leaf count {
             description
               "count of this member VNF  within this scaling group.
                The count allows to define  the number of instances
                when a scaling action targets this scaling group";
             type uint32;
             default 1;
           }
         }
 
         leaf min-instance-count {
           description
             "Minimum instances of the scaling group which are allowed.
             These instances are created by default when the network service
             is instantiated.";
           type uint32;
           default 0;
         }
 
         leaf max-instance-count {
           description
             "Maximum instances of this scaling group that are allowed
              in a single network service. The network service scaling
              will fail, when the number of service group instances
              exceed the max-instance-count specified.";
           type uint32;
           default 10;
         }
 
         list scaling-config-action {
           description "List of scaling config actions";
           key "trigger";
 
           leaf trigger {
             description "scaling trigger";
             type scaling-trigger;
           }
 
           leaf ns-config-primitive-name-ref {
             description "Reference to the NS config name primitive";
             type leafref {
               path "../../../config-primitive/name";
             }
           }
         }
       }
 
       list placement-groups {
         description "List of placement groups at NS level";
 
         key "name";
         uses manotypes:placement-group-info;
         
         list constituent-vnfd {
           description
               "List of VNFDs that are part of thisplacement group";
 
           key "member-vnf-index-ref";
 
           leaf member-vnf-index-ref {
             description "member VNF index of this member VNF";
             type leafref {
               path "../../../constituent-vnfd/member-vnf-index";
             }
           }
 
           leaf vnfd-id-ref {
             description
                 "Identifier for the VNFD.";
             type leafref {
               path "/vnfd:vnfd-catalog/vnfd:vnfd/vnfd:id";
             }
           }
         }
       }
       
 
       list vnf-dependency {
         description
             "List of VNF dependencies.";
         key vnf-source-ref;
         leaf vnf-source-ref {
           type leafref {
             path "/vnfd:vnfd-catalog/vnfd:vnfd/vnfd:id";
           }
         }
         leaf vnf-depends-on-ref {
           description
               "Reference to VNF that sorce VNF depends.";
           type leafref {
             path "/vnfd:vnfd-catalog/vnfd:vnfd/vnfd:id";
           }
         }
       }
 
       list vnffgd {
         description
             "List of VNF Forwarding Graph Descriptors (VNFFGD).";
 
         key "id";
 
         leaf id {
           description 
               "Identifier for the VNFFGD.";
           type string;
         }
 
         leaf name {
           description 
               "VNFFGD name.";
           type string;
         }
 
         leaf short-name {
           description 
               "Short name for VNFFGD for UI";
           type string;
         }
 
         leaf vendor {
           description "Provider of the VNFFGD.";
           type string;
         }
 
         leaf description {
           description "Description of the VNFFGD.";
           type string;
         }
 
         leaf version {
           description "Version of the VNFFGD";
           type string;
         }
 
         list rsp {
           description
               "List of Rendered Service Paths (RSP).";
 
           key "id";
 
           leaf id {
             description
                 "Identifier for the RSP.";
             type string;
           }
 
           leaf name {
             description
                 "RSP name.";
             type string;
           }
 
           list vnfd-connection-point-ref {
             description
                   "A list of references to connection points.";
             key "member-vnf-index-ref";
 
             leaf member-vnf-index-ref {
               description "Reference to member-vnf within constituent-vnfds";
               type leafref {
                 path "../../../../nsd:constituent-vnfd/nsd:member-vnf-index";
               }
             }
 
             leaf order {
               type uint8;
               description
                   "A number that denotes the order of a VNF in a chain";
             }
 
              leaf vnfd-id-ref {
                description 
                    "A reference to a vnfd. This is a 
                     leafref to path:
                         ../../../../nsd:constituent-vnfd
                         + [nsd:id = current()/../nsd:id-ref]
                         + /nsd:vnfd-id-ref
                     NOTE: An issue with confd is preventing the
                     use of xpath. Seems to be an issue with leafref
                     to leafref, whose target is in a different module.
                     Once that is resovled this will switched to use
                     leafref";
                type yang:uuid;
              }
 
              leaf vnfd-connection-point-ref {
                description 
                    "A reference to a connection point name 
                     in a vnfd. This is a leafref to path:
                         /vnfd:vnfd-catalog/vnfd:vnfd
                         + [vnfd:id = current()/../nsd:vnfd-id-ref]
                         + /vnfd:connection-point/vnfd:name
                     NOTE: An issue with confd is preventing the
                     use of xpath. Seems to be an issue with leafref
                     to leafref, whose target is in a different module.
                     Once that is resovled this will switched to use
                     leafref";
                 type string;
             }
           }
         } //rsp
 
         list classifier {
           description
               "List of classifier rules.";
 
           key "id";
 
           leaf id {
             description
                 "Identifier for the classifier rule.";
             type string;
           }
 
           leaf name {
             description
                 "Name of the classifier.";
             type string;
           }
 
           leaf rsp-id-ref {
             description
                 "A reference to the RSP.";
             type leafref {
               path "../../nsd:rsp/nsd:id";
             }
           }
 
           
           leaf member-vnf-index-ref {
             description "Reference to member-vnf within constituent-vnfds";
             type leafref {
               path "../../../nsd:constituent-vnfd/nsd:member-vnf-index";
             }
           }
 
           leaf vnfd-id-ref {
             description 
                 "A reference to a vnfd. This is a 
                     leafref to path:
                         ../../../nsd:constituent-vnfd
                         + [nsd:id = current()/../nsd:id-ref]
                         + /nsd:vnfd-id-ref
                     NOTE: An issue with confd is preventing the
                     use of xpath. Seems to be an issue with leafref
                     to leafref, whose target is in a different module.
                     Once that is resovled this will switched to use
                     leafref";
             type yang:uuid;
           }
 
           leaf vnfd-connection-point-ref {
             description 
                 "A reference to a connection point name 
                     in a vnfd. This is a leafref to path:
                         /vnfd:vnfd-catalog/vnfd:vnfd
                         + [vnfd:id = current()/../nsd:vnfd-id-ref]
                         + /vnfd:connection-point/vnfd:name
                     NOTE: An issue with confd is preventing the
                     use of xpath. Seems to be an issue with leafref
                     to leafref, whose target is in a different module.
                     Once that is resovled this will switched to use
                     leafref";
             type string;
           }
              
           list match-attributes {
             description
                 "List of match attributes.";
 
             key "id";
 
             leaf id {
               description
                   "Identifier for the classifier match attribute rule.";
               type string;
             }
 
             leaf ip-proto {
               description
                   "IP Protocol.";
               type uint8;
             }
 
             leaf source-ip-address {
               description
                   "Source IP address.";
               type inet:ip-address;
             }
 
             leaf destination-ip-address {
               description
                   "Destination IP address.";
               type inet:ip-address;
             }
 
             leaf source-port {
               description
                   "Source port number.";
               type inet:port-number;
             }
 
             leaf destination-port {
               description
                   "Destination port number.";
               type inet:port-number;
             }
             //TODO: Add more match criteria
           } //match-attributes
         } // classifier
       } // vnffgd
 
       uses manotypes:monitoring-param;
       uses manotypes:input-parameter-xpath;
 
       list parameter-pool {
         description
           "Pool of parameter values which must be 
            pulled from during configuration";
         key "name";
 
         leaf name {
           description
               "Name of the configuration value pool";
           type string;
         }
 
         container range {
           description
               "Create a range of values to populate the pool with";
 
           leaf start-value {
             description
                 "Generated pool values start at this value";
             type uint32;
             mandatory true;
           }
 
           leaf end-value {
             description
                 "Generated pool values stop at this value";
             type uint32;
             mandatory true;
           }
         }
       }
 
       list config-primitive {
         description
             "Network service level configuration primitives.";
 
         key "name";
 
         leaf name {
           description
               "Name of the configuration primitive.";
           type string;
         }
 
         list parameter {
           description
               "List of parameters to the configuration primitive.";
 
           key "name";
           uses manotypes:primitive-parameter;
         }
 
         list parameter-group {
           description
               "Grouping of parameters which are logically grouped in UI";
           key "name";
 
           leaf name {
             description
                 "Name of the parameter group";
             type string;
           }
 
           list parameter {
             description
                 "List of parameters to the configuration primitive.";
             key "name";
             uses manotypes:primitive-parameter;
           }
 
           leaf mandatory {
             description "Is this parameter group mandatory";
             type boolean;
             default true;
           }
         }
 
         list vnf-primitive-group {
           description
               "List of configuration primitives grouped by VNF.";
 
           key "member-vnf-index-ref";
           leaf member-vnf-index-ref {
             description
                 "Reference to member-vnf within constituent-vnfds";
             type uint64;
           }
 
           leaf vnfd-id-ref {
             description
                 "A reference to a vnfd. This is a 
                  leafref to path:
                      ../../../../nsd:constituent-vnfd
                      + [nsd:id = current()/../nsd:id-ref]
                      + /nsd:vnfd-id-ref
                  NOTE: An issue with confd is preventing the
                  use of xpath. Seems to be an issue with leafref
                  to leafref, whose target is in a different module.
                  Once that is resovled this will switched to use
                  leafref";
 
             type string;
           }
 
           leaf vnfd-name {
             description
                 "Name of the VNFD";
             type string;
           }
 
           list primitive {
             key "index";
 
             leaf index {
               description "Index of this primitive";
               type uint32;
             }
 
             leaf name {
               description "Name of the primitive in the VNF primitive ";
               type string;
             }
           }
         }
 
         leaf user-defined-script {
           description
               "A user defined script.";
           type string;
         }
       }
     }
   }
 }

## VNFD YANG Model

module vnfd
 {
   namespace "urn:ietf:params:xml:ns:yang:nfvo:vnfd";
   prefix "vnfd";
 
   import mano-types {
     prefix "manotypes";
   }
 
   import rw-pb-ext {
     prefix "rwpb";
   }
 
   import ietf-yang-types {
     prefix "yang";
   }
 
   import ietf-inet-types {
     prefix "inet";
   }
 
   revision 2015-09-10 {
     description
       "Initial revision. This YANG file defines
        the Virtual Network Function (VNF)";
     reference
       "Derived from earlier versions of base YANG files";
   }
 
   grouping common-connection-point {
     leaf name {
       description "Name of the connection point";
       type string;
     }
     
     leaf id {
       description "Identifier for the internal connection points";
       type string;
     }
 
     leaf short-name {
       description "Short name of the connection point";
       type string;
     }
     
     leaf type {
       description "Type of the connection point.";
       type manotypes:connection-point-type;
     }
   }
   
   grouping virtual-interface {
     container virtual-interface {
       description
           "Container for the virtual interface properties";
 
       leaf type {
         description
             "Specifies the type of virtual interface
              between VM and host.
              VIRTIO          : Use the traditional VIRTIO interface.
              PCI-PASSTHROUGH : Use PCI-PASSTHROUGH interface.
              SR-IOV          : Use SR-IOV interface.
              OM-MGMT         : Used to specify openmano mgmt external-connection type";
 
         type enumeration {
           enum OM-MGMT;
           enum PCI-PASSTHROUGH;
           enum SR-IOV;
           enum VIRTIO;
         }
         default "VIRTIO";
       }
 
       leaf vpci {
         description
             "Specifies the virtual PCI address. Expressed in
              the following format dddd:dd:dd.d. For example
              0000:00:12.0. This information can be used to
              pass as metadata during the VM creation.";
         type string;
       }
 
       leaf bandwidth {
         description
             "Aggregate bandwidth of the NIC.";
         type uint64;
       }
     }
   }
 
   container vnfd-catalog {
 
     description
         "Virtual Network Function Descriptor (VNFD).";
 
     list vnfd {
       key "id";
 
       leaf id {
         description "Identifier for the VNFD.";
         type yang:uuid;
       }
 
       leaf name {
         description "VNFD name.";
         mandatory true;
         type string;
       }
 
       leaf short-name {
         description "VNFD short name.";
         type string;
       }
 
       leaf vendor {
         description "Vendor of the VNFD.";
         type string;
       }
 
       leaf logo {
         description
             "Vendor logo for the Virtual Network Function";
         type string;
       }
 
       leaf description {
         description "Description of the VNFD.";
         type string;
       }
 
       leaf version {
         description "Version of the VNFD";
         type string;
       }
 
       container mgmt-interface {
         description
             "Interface over which the VNF is managed.";
 
         uses manotypes:vnf-configuration;
         
         choice endpoint-type {
           description
               "Indicates the type of management endpoint.";
 
           case ip {
             description
                 "Specifies the static IP address for managing the VNF.";
             leaf ip-address {
               type inet:ip-address;
             }
           }
 
           case vdu-id {
             description
                 "Use the default management interface on this VDU.";
             leaf vdu-id {
               type leafref {
                 path "/vnfd:vnfd-catalog/vnfd:vnfd/vnfd:vdu/vnfd:id";
               }
             }
           }
 
           case cp {
             description
                 "Use the ip address associated with this connection point.";
             leaf cp {
               type leafref {
                 path "/vnfd:vnfd-catalog/vnfd:vnfd/vnfd:connection-point/vnfd:name";
               }
             }
           }
         }
 
         leaf port {
           description
               "Port for the management interface.";
           type inet:port-number;
         }
 
         container dashboard-params {
           description "Parameters for the VNF dashboard";
 
           leaf path {
             description "The HTTP path for the dashboard";
             type string;
           }
 
           leaf https {
             description "Pick HTTPS instead of HTTP , Default is false";
             type boolean;
           }
 
           leaf port {
             description "The HTTP port for the dashboard";
             type inet:port-number;
           }
         }
       }
 
       list internal-vld {
         key "id";
         description
             "List of Internal Virtual Link Descriptors (VLD).
             The internal VLD describes the basic topology of
             the connectivity (e.g. E-LAN, E-Line, E-Tree)
             between internal VNF components of the system.";
 
         leaf id {
           description "Identifier for the VLD";
           type string;
         }
 
         leaf name {
           description "Name of the internal VLD";
           type string;
         }
 
         leaf short-name {
           description "Short name of the internal VLD";
           type string;
         }
 
         leaf description {
           type string;
         }
 
         leaf type {
           type manotypes:virtual-link-type;
         }
 
         leaf root-bandwidth {
           description
               "For ELAN this is the aggregate bandwidth.";
           type uint64;
         }
 
         leaf leaf-bandwidth {
           description
               "For ELAN this is the bandwidth of branches.";
           type uint64;
         }
 
         leaf-list internal-connection-point-ref {
           type leafref {
             path "../../vdu/internal-connection-point/id";
           }
         }
 
         uses manotypes:provider-network;
       }
 
       list connection-point {
         key "name";
         description
             "List for external connection points. Each VNF has one
             or more external connection points. As the name
             implies that external connection points are used for
             connecting the VNF to other VNFs or to external networks.
             Each VNF exposes these connection points to the
             orchestrator. The orchestrator can construct network
             services by connecting the connection points between
             different VNFs. The NFVO will use VLDs and VNFFGs at
             the network service level to construct network services.";
 
         uses common-connection-point;
       }
 
       list vdu {
         description "List of Virtual Deployment Units";
         key "id";
 
         leaf id {
           description "Unique id for the VDU";
           type string;
         }
 
         leaf name {
           description "Unique name for the VDU";
           type string;
         }
 
         leaf description {
             description "Description of the VDU.";
             type string;
         }
 
         leaf count {
           description "Number of instances of VDU";
           type uint64;
         }
 
         leaf mgmt-vpci {
           description
               "Specifies the virtual PCI address. Expressed in
              the following format dddd:dd:dd.d. For example
              0000:00:12.0. This information can be used to
              pass as metadata during the VM creation.";
           type string;
         }
 
 
         uses manotypes:vm-flavor;
         uses manotypes:guest-epa;
         uses manotypes:vswitch-epa;
         uses manotypes:hypervisor-epa;
         uses manotypes:host-epa;
 
         leaf image {
           description
             "Image name for the software image.
              If the image name is found within the VNF packaage it will
              be uploaded to all cloud accounts during onboarding process.
              Otherwise, the image must be added to the cloud account with
              the same name as entered here.
             ";
           mandatory true;
           type string;
         }
 
         leaf image-checksum {
           description
             "Image md5sum for the software image.
             The md5sum, if provided, along with the image name uniquely
             identifies an image uploaded to the CAL.
             ";
           type string;
         }
 
         leaf cloud-init {
           description "Content of cloud-init script";
           type string;
         }
 
         list internal-connection-point {
           key "id";
           description
               "List for internal connection points. Each VNFC
               has zero or more internal connection points.
               Internal connection points are used for connecting
               the VNF components internal to the VNF. If a VNF
               has only one VNFC, it may not have any internal
               connection points.";
 
           uses common-connection-point;
 
           leaf internal-vld-ref {
             type leafref {
               path "../../../internal-vld/id";
             }
           }
         }
 
         list internal-interface {
           description
               "List of internal interfaces for the VNF";
           key name;
 
           leaf name {
             description
                 "Name of internal interface. Note that this
                 name has only local significance to the VDU.";
             type string;
           }
 
           leaf vdu-internal-connection-point-ref {
             type leafref {
               path "../../internal-connection-point/id";
             }
           }
           uses virtual-interface;
         }
 
         list external-interface {
           description
               "List of external interfaces for the VNF.
               The external interfaces enable sending
               traffic to and from VNF.";
           key name;
 
           leaf name {
             description
                 "Name of the external interface. Note that
                 this name has only local significance.";
             type string;
           }
 
           leaf vnfd-connection-point-ref {
             description
               "Name of the external connection point.";
             type leafref {
               path "../../../connection-point/name";
             }
           }
           uses virtual-interface;
         }
       }
 
       list vdu-dependency {
         description
             "List of VDU dependencies.";
 
         key vdu-source-ref;
         leaf vdu-source-ref {
           type leafref {
             path "../../vdu/id";
           }
         }
 
         leaf vdu-depends-on-ref {
           description
               "Reference to the VDU that
               source VDU depends.";
           type leafref {
             path "../../vdu/id";
           }
         }
       }
 
       leaf service-function-chain {
         description "Type of node in Service Function Chaining Architecture";
 
         type enumeration {
           enum UNAWARE;
           enum CLASSIFIER;
           enum SF;
           enum SFF;
         }
         default "UNAWARE";
       }
       
       leaf service-function-type {
         description
             "Type of Service Function.
              NOTE: This needs to map with Service Function Type in ODL to
              support VNFFG. Service Function Type is manadatory param in ODL
              SFC. This is temporarily set to string for ease of use";
             type string;
       }
 
       uses manotypes:monitoring-param;
 
       list placement-groups {
         description "List of placement groups at VNF level";
 
         key "name";
         uses manotypes:placement-group-info;
         
         list constituent-vdus {
           description
               "List of VDUs that are part of this placement group";
           key "member-vdu-ref";
         
           leaf member-vdu-ref {
             type leafref {
               path "../../../vdu/id";
             }
           }
         }
       }
     }
   }
 }