## Slide 1: A 5G experimental environment focused on vertical applications
Diego R. Lopez, Telefónica I+D
5GINFIRE has received funding from the European Horizon 2020 Programme for research, technological development and demonstration under grant agreement no 732497

## Slide 2: Emerging Trends in 5G
One network to support all cases
  Focused on vertical industry requirements
Consolidation of base technologies
  Software Network
  NFV + SDN
  Edge Computing
  …
The challenge of operationalization
  Supporting vertical users
  5GINFIRE is committed to build and operate an open and extensible 5G NFV-based ecosystem of experimental facilities

## Slide 3: Requirements for the Facility
Adopt and be interoperable with current standards
  Cloud, SDN, NFV, MEC…
Use open standards and integrate technologically mature, widespread open source toolsets
  Hence OSM
Simplify the deployment of experimentation scenarios
  And guarantee repeatability
Enable vertical experimenters at all levels
  Applications, services or VNFs
  5G-enabled experimentation infrastructure also able to support specialized infrastructure for verticals

## Slide 4: Targeted Use Case Assisted Overtaking

## Slide 5: 5GinFIRE Reference Model
Open source components
  OpenStack, OpenDaylight…
  OSM
Integrating infrastructures from verticals
Generalizing the concept of VNFs taking into account functionalities other than network
  Vertical focus
  Introducing VxFs
  Universal management of virtual functions
Automated deployment of VxFs
  Dedicated VxF stores

## Slide 6: Actors in an Experiment Workflow
Experimenter
5GinFIRE operations
Select/Deploy
VxFs
Experiment
description
Upload
Submit for validation
Manage
deployment
Get access to testbed resources, Monitor,
experiment
Create experiment
5GinFIRE
Testbed providers
Create account
Authorize
account
Validate experiment
Validate experiment
(feasibility schedule dates, etc.)
Orchestrate
deployment
Schedule/
Create
deployment
Release
experiment
Access revoked
Results available
Manage resources/installations etc.
Iterate
Submit
Approved
Notify
Schedule etc.

## Slide 7: Middleware and Portal Features
Single point of interaction for experimenters
  Manage and monitor experiments
  Update and browse the VxF repository
Support for 5GINFIRE admins
  5GINFIRE platform and repository
Gatekeeper for VxF developers
  Support a DevOps approach
Model-based
  Map experiment descriptors onto NSDs
  Consistent verification and deployment
Integration with other testbeds
  Enabling the creation of federated experiments (Fed4FIRE)
  5GINFIRE repository accessible through other FIRE catalogues

## Slide 8: The 5GinFIRE Portal
Portal API backend
OSM
API
API
Portal web
frontend
OSM
(launchpad) client API
Public VxF descriptors repository
IDP
Angular
JavaWS
YANG RIFT.IO model to Java

## Slide 9: The 5GinFIRE NFVO
VIM
OSM stack
5TONIC datacenter
VIM
ITAv datacenter
VIM
UNIBRIS/BiO datacenter
Other datacenters
(UFU & open calls)
OpenStack Ocata
OSM Release TWO

## Slide 10: Control Plane Connectivity
OSM stack
NFVI
Compute
nodes
Data Plane Switch
NAT
VPN
NFVI
Compute
nodes
Data Plane Switch
NFVI
Compute
nodes
Data Plane Switch
VIM management
Infrastructure management
Telco/VNF management
ITAv
UNIVBRIS
UC3M
VIM
VIM
VIM
VIM

## Slide 11: Orchestration @ 5TONIC
IMDEA NFVI
Compute
nodes
Data Plane Switch
∂∂©
VPN gateway
5GINFIRE NFVI
Compute
nodes
Data Plane Switch
Internet
Ocata
Relesase TWO
Ocata
Additional infrastructure (not shown in the figure):
  3x server computers to support complementary functionalities, such as aiding experimentation (e.g. hosting client applications), deployment of a network management system (e.g, Nagios, Check_MK), data storage (e.g. backups, VM images or code), etc.
Public cloud nodes

## Slide 12: What Could Come to OSM
Validation in a 5G playground
  Interaction with 5G OSS-like environments, including the slice matters
  Multi-* (VIM, VCA, RO, domain, tenant, tier…) operation
  With vertical, layman users
  Testing of new features in this and coming releases
Explore DevOps lifecycles and mediation elements
  Incorporate Verification & Validation procedures to service lifecycles
  Application of intent declarations in combination with descriptors
Security enhancements
  Security models
  Token services
  Assured auditability
Additional application environments
  Micro VNFs

## Slide 13: Virtuous Circles
Open source is a natural way to make available research project results
  And to increase their impact on standardization
Research projects open new ways for the evolution of open source
  Stretching the scopes
  Exploring additional scenarios and technologies
Network function and service orchestration is a hot research topic
  With 5G as the flagship
As long as we define proper (and simple) rules of engagement
  Take the software, do whatever you feel like with it
  Come back to the community, make your case
  Abide to upstream community practice

## Slide 14: ‘Nuff said!
https://5ginfire.eu/
contact@5GinFIRE.eu
https://twitter.com/5GinFIRE
5GINFIRE has received funding from the European Horizon 2020 Programme for research, technological development and demonstration under grant agreement no 732497